## Slide 1: ECEN 3593-001 Computer Organization
Lecture #13
15 February 2021

## Slide 2: Agenda
Class Announcements
Phase 4 Schematic Tool Demo
Pipelined Processor

## Slide 3: Class Announcements
Reading for the week
  “Computer Organization and Design, The Hardware / Software Interface, RISC-V edition,” by David Patterson and John Hennessy
    ISBN 978-0-12-812275-4
    Appendix A – “The Basics of Logic Design”
    pages A-1 through A-37 (sections A.1 through A.5)

## Slide 4: Class Announcements
Wednesday is Wellness Day – feel free to take a break and recharge
No class session, but Office Hours are available by request

## Slide 5: Class Announcements
Phase 4 Target Date Sunday, February 21 at 10:00 PM
Homework #2 due Thursday, February 18 at 10:00 PM
Phase 3 in the deduction period – 2% as of today
Deduction reduced – 2%/day until Friday, then 5%/day
Read the document carefully – there are several ways to lose points
Phase 5 will be posted Wednesday evening.
Target Date Sunday, February 28 at 10:00 PM

## Slide 6: Executing an Instruction (ME Stage)
PC  instruction memory, fetch instruction
Register numbers  register file, read registers
Depending on instruction class
  Use ALU to calculate
    Arithmetic result
    Memory address for load/store
    Branch target address
Access data memory for load/store
Update PC  target address or PC + 4
Update Register File

## Slide 7: Memory (ME) Stage - Memory
ALU
Data Memory
addr
din
dout
memwr
ctrl5
memrd
ctrl6
Memory (MEM/ME)
ALU output is the pipeline register
Provide the DM address
Provide the DM write data
Read or write memory data

## Slide 8: Executing an Instruction (ME Stage)
PC  instruction memory, fetch instruction
Register numbers  register file, read registers
Depending on instruction class
  Use ALU to calculate
    Arithmetic result
    Memory address for load/store
    Branch target address
Access data memory for load/store
Update PC  target address or PC + 4
Update Register File

## Slide 9: Memory (ME) Stage - Branch
ALU
MUX
ADD
PC
ctrl1
zero
Zero output is the pipeline register
Add branch offset to PC
Zero selects the next PC input (branch or not)

## Slide 10: Executing an Instruction (WB Stage)
PC  instruction memory, fetch instruction
Register numbers  register file, read registers
Depending on instruction class
  Use ALU to calculate
    Arithmetic result
    Memory address for load/store
    Branch target address
Access data memory for load/store
Update PC  target address or PC + 4
Update Register File

## Slide 11: Writeback (WB) Stage
MUX
Register File
dout2
Data Memory
addr
din
dout
dout1
ctrl2
memwr
regwr
memrd
Writeback (WB)
rd
rs1
rs2
din
Memory output is the pipeline register
Mux selects RF input – memory or ALU
Data written back to Register File

## Slide 12: Phase 4
New #phase4 channel in Slack
Phase 4 involves building the schematic of a subset of RISC-V which executes 2 instructions (ADD and ADDI)
Schematics are drawn using app.diagrams.net in a Browser
The result is the standardname4.xml file
Submit by sending me a DM in Slack with standardname4.xml attached

## Slide 13: Schematics
IF
ID
EX
ME
WB

## Slide 14: Component Library
Copy components from here to the other pages
Connect components using “signals” – input, output and internal
Label all signals
Distinguish “signals” and “registers”

## Slide 15: Schematic Demonstration
Application is app.diagrams.net
Incorrectly listed as app.diagram.net in the Phase 4 document

## Slide 16: Developing a 32-bit ALU
We will step through the process of designing the internals of an ALU
This material is in Appendix A of the textbook

## Slide 17: Developing a 32-bit ALU
A 1-bit logical unit to calculate AND if operation = 0 and OR if operation = 1

## Slide 18: Developing a 32-bit ALU
Next we need a full bit adder
Sum = a ^ b
Includes a CarryIn bit from the previous 1-bit adder and CarryOut bit for the next

## Slide 19: Developing a 32-bit ALU
Now we have an ALU that can AND, OR, and ADD whose output is specified by the control lines, Operation
  Operation = 0b00, AND
  Operation = 0b01, OR
  Operation = 0b10, ADD

## Slide 20: Developing a 32-bit ALU
Now we need subtraction
By asserting Binvert and in the least significant bit set CarryIn, we have 2s complement substraction
  Control bits: Binvert, Operation, CarryIn
  Op = 0b0000, AND
  Op = 0b0010, OR
  Op = 0b0100, ADD
  Op = 0b1101, Sub

## Slide 21: Developing a 32-bit ALU
Now, we could implement a NOR instruction by providing both Ainvert and Binvert
  Control bits: Ainvert, Binvert, Operation
  0b0000, AND
  0b1100, NOR, not defined per the ISA
  0b0001, OR
  0b0010, ADD
  0b0110, Sub (a – b)
  0b1101, NAND, not defined per the ISA
  0b1010, sub (b – a), not defined per the ISA

## Slide 22: Developing a 32-bit ALU
Here is what the 32-bit Carry flow through ALU would look like
Set is the sign of the output (Result31) but is only used in some cases – when? (Poll)
SLT
Why do we have SLT and not SGT? (Poll)

## Slide 23: Developing a 32-bit ALU
By NORing all the outputs, the subtraction of registers a and b can be used to branch on equal
Equal numbers will equal 0, not equal numbers would be a 1

## Slide 24: Developing a 32-bit ALU
Note arithmetic operations such as loads, stores, and beq use the ALU and must map into the ALU control lines