## Slide 1: ECEN 3593-001 Computer Organization
Lecture #14
19 February 2021

## Slide 2: Agenda
Class Announcements
Phase 4
Chapter 4

## Slide 3: Class Announcements
Phase 3 grades are posted (if you have completed it)
Scoring details in #phase3
Send a DM of “Phase3?” if you want your specific details
Starting tonight at 10:00 PM, Phase 3 deduction (which is now 10%) will increase to 5%/day

## Slide 4: Class Announcements
Homework #2 is graded and reviewed
Answers will be enabled over the weekend when everyone has submitted

## Slide 5: Class Announcements
Phase 5 of the project is posted
  Target date is Sunday, February 28 at 10:00 PM
  Bonus before the Target Date – 1%/day (Maximum 7%)
  Deduction after the Target Date – 4%/day
  A fresh starting project (including the IA Model) is included
  Phase 5 is the CA implementation of ADD/ADDI/HALT
  Project must be completed completely to receive any score
  Next week several class sessions will include topics related to the Cycle Accurate (CA) model in Codasip

## Slide 6: Why Create Schematics/Block Diagrams?
This is the real world process
Block diagrams are much easier to understand
  What great idea of Computer Architecture is at work here? (Poll)
  ABSTRACTION
A known correct schematic makes the Codasip Codal implementation much easier

## Slide 7: Phase 4
Questions?

## Slide 8: ALU Control
ALU used for:
  Load/Store: F = add
  Branch: F = subtract, xor, slt
  R-type: F depends on opcode / funct3, funct7

## Slide 9: Full Data path with Control
This is a model of a single cycle CPU.
All instructions are completed in one clock cycle
You can view the ISA or Instruction Accurate model simulator as a single cycle CPU implementation
We will merge the ALU control decoding into the main Control DECODER
The DECODER will get bits [31:25], [14:12] and [6:0].
What instructions fields are these? (Poll)

## Slide 10: Reviewing Single Cycle CPU model
Single-Cycle implementation refers to a CPU where one instruction is execute in once clock cycle
Clock period is determined by the longest instruction
  Instruction memory  register file  ALU  register file
  Instruction memory  register file  ALU  data memory  register file
  Load/Stores require an extra step, access to data memory
Not feasible to vary period for different instructions
  Thus, the load/store instruction defines the clock period / frequency in a single cycle machine
Violates design principle
  Making the common case fast
  Common case equals the slowest instruction in this design
Performance via pipelining can improve this performance bottleneck

## Slide 11: Performance Improvement via Pipelining
Pipelining is an implementation technique in which multiple instructions overlap in execution
Four loads:
  Speedup = 16/7 ~ 2.3x
Non-stop:
  Speedup = approaches the number of stages

## Slide 12: RISC-V Pipeline
Stages are the steps in a pipeline that when an instruction goes through all the stages, the instruction is completed
Five stages, one step per stage
  IF: Instruction fetch from memory
  ID: Instruction decode & register read
  EX: Execute operation or calculate address
  MEM(ME): Access memory operand
  WB: Write result back to register

## Slide 13: Pipeline Performance
Assume time for stages is
  100ps for register read or write
  200ps for other stages
Compare pipelined data path with single-cycle data path

## Slide 14: Pipeline Performance
Single-cycle (Tc= 800ps)
Pipelined (Tc= 200ps)

## Slide 15: Pipeline Speedup
If all stages are balanced
  i.e., all take the same time
  Time between instructionspipelined = Time between instructionsnonpipelined Number of stages
If not balanced, speedup is less
Speedup due to increased throughput
  Latency (time for each instruction) does not decrease
  Latency will actually increase for non-balanced stage design
  But Throughput is increased!

## Slide 16: Pipelining and ISA Design
RISC-V ISA designed for pipelining
  All instructions are 32-bits
    Easier to fetch and decode in one cycle
    c.f. x86: 1- to 15-byte instructions
  Few and regular instruction formats
    Can decode and read registers in one step
  Load/store addressing
    Can calculate address in 3rd stage, access memory in 4th stage

## Slide 17: Pipelined Data Path
Book IF/ID -> our ID
Book ID/EX -> our EX
Book EX/MEM -> our ME
Book MEM/WB -> our WB

## Slide 18: Pipelining Hazards
In a pipeline, there are situations that prevent starting the next instruction in the next cycle
Structural hazards
  A required resource is busy
Data hazards
  Need to wait for previous instruction to complete its data read/write
Control hazards
  Deciding on control action depends on previous instruction

## Slide 19: Structural Hazards
Structural hazards occur when a conflict of a resource prevent one of the instructions from proceeding down the pipe
In the RISC-V pipeline with a single memory
  Load/store requires data access
  Instruction fetch would have to stall for that cycle
    Would cause a pipeline “bubble”
Hence, pipelined data paths require separate instruction/data memories
  Or separate instruction/data caches

## Slide 20: Structural Hazard
Adder and ALU
Could share them, but that would be a structural hazard

## Slide 21: Data Hazards
Data hazards occur when the pipeline must be stalled because one stage must wait for another stage to complete
  add x19, x0, x1 sub x2, x19, x3
Results from the dependency of one instruction on an earlier instruction that is still in the pipeline
Cannot start the sub instruction here

## Slide 22: Forwarding (aka Bypassing)
Observe that the data is available before the instruction is completed
Use result when it is computed, not waiting for the instruction to complete
  Don’t wait for it to be stored in a register
  Requires extra connections in the data path
Forwarding/Bypassing
Forwarding paths are only valid if the destination stage is later in time than the source stage

## Slide 23: Load Use Data Hazard
Can’t always avoid stalls by forwarding
  If value not computed when needed
  Can’t forward backward in time!
  The pipeline must stall for 1 cycle
If no forwarding, how many clock cycles would the CPU need to stall due to a Load Hazard? (Poll)

## Slide 24: FBQ
First three correct answers submitted to #phase5 (NOT #phase2)
10 bonus points in Phase 5
Each person can only win the bonus points once