## Slide 1: ECEN 3593-001 Computer Organization
Lecture #15
22 February 2021

## Slide 2: Agenda
Class Announcements
Phase 5
Chapter 4 – Pipelining

## Slide 3: Class Announcements
Reading for the week
  “Computer Organization and Design, The Hardware / Software Interface, RISC-V edition,” by David Patterson and John Hennessy
    ISBN 978-0-12-812275-4
    Chapter 4, “The Processor”
    pages 236-314 (sections 4.1 thru 4.8)
Homework #2 correct answers enabled in Canvas

## Slide 4: Class Announcements
A useful tool has been posted under “Instruction Translator” in Canvas
This is an Excel-based disassembler which translates Machine code to Assembly code
Handy for understanding the Assembly <-> Machine function
Includes a User’s Guide

## Slide 5: Class Announcements
Phase 3 is in the deduction period – 20% + 5%/day
Phase 4 is in the deduction period – 4%/day
If you have successfully completed Phase 4 your scores are posted in Canvas
Phase 5 Target Date is Sunday, February 28 at 10:00 PM
Homework #3 will be posted next week
My OH MWF 2:00 to 3:00. This week I will have an open Zoom meeting each day at https://cuboulder.zoom.us/j/4317981384
Also can request meeting any time

## Slide 6: Phase 5 Process
Update each of the files in the ca area
  Use the Phase 4 schematics!
Get this to build (Simulator (ca))
Edit files until it does
Run phase5_test on CA Simulator
Debug
Repeat until success and submit
Debug is likely to take quite a while – don’t wait

## Slide 7: Codasip CA Model
Decode the instruction to create all control signals
Main processing loop
Defines the various control enums and bit field widths
Debug utilities
Stall/flush functions
Actual pipeline processes
Register and signal definitions

## Slide 8: Codasip Operation
Starts with “main” function in ca_main_reset.codal
Calls each pipeline function in order and executes its code
Then ALL registers are updated with their new input values SIMULTANEOUSLY
One clock cycle has now been executed
Loop back and repeat until HALT
Why are the stages in reverse?

## Slide 9: Evaluating Right to Left
Normal data flows left to right (IF -> WB) through the pipeline registers
But some data is required by a later (i.e. to the left) cycle
Thus the rightmost value (e.g. WB) must be computed first

## Slide 10: Phase 5
Questions?

## Slide 11: Load Use Data Hazard
Can’t always avoid stalls by forwarding
  If value not computed when needed
  Can’t forward backward in time!
  The pipeline must stall for 1 cycle

## Slide 12: The compiler comes to the rescue – at least sometimes
Reorder code to avoid use of load result in the next instruction
C code for A = B + E; C = B + F;
ld x1, 0(x0)
ld x2, 8(x0)
add x3, x1, x2
sd x3, 24(x0)
ld x4, 16(x0)
add x5, x1, x4
sd x5, 32(x0)
stall
stall
9 cycles
ld x1, 0(x0)
ld x2, 8(x0)
ld x4, 16(x0)
add x3, x1, x2
sd x3, 24(x0)
add x5, x1, x4
sd x5, 32(x0)
7 cycles

## Slide 13: Control Hazards
Control hazards arise from the need to make a decision based on the results of one instruction that affect instructions already in the pipeline
Branch determines flow of control
  Fetching next instruction depends on branch outcome
  Pipeline can’t always fetch correct instruction
In RISC-V pipeline
  Need to compare registers and compute target early in the pipeline
  Could add hardware to do it in ID stage (only realistic for BEQ/BNE)
  But – we will not do this in our design

## Slide 14: The CPU could stall a cycle to determine what address to fetch after the branch?
Wait until branch outcome determined before fetching next instruction
This would effectively make all branch instructions a CPI of 2

## Slide 15: MIPS Solution – Branch Delay Slot
The MIPS architecture implements a Branch Delay Slot
beq x1, x2, -40
add x5, x6, x7 <- this instruction is always
executed, even if the branch is
taken
If the assembler can’t find an instruction that works here, a NOP must be inserted

## Slide 16: Predict the next address after the branch
Branch prediction is a method of resolving a branch hazard that assumes a given outcome from the branch and proceeds from that assumption rather than waiting to be certain the actual outcome
Longer pipelines can’t readily determine branch outcome early
  Stall penalty becomes unacceptable
Predict outcome of branch
  Only stall if prediction is wrong
In RISC-V pipeline
  Can predict branches not taken
  Fetch instruction after branch, with no delay

## Slide 17: Predict Not Taken
20: add x1, x2, x3
IF
ID
EX
ME
WB
IF
ID
EX
ME
WB
24: beq x4, x5, 60
IF
ID
EX
28: and x7, x8, x9
IF
ID
32: slt x8, x7, x10
IF
IF
36: add x12, x13, x20
60: xori x14, x13, 0xFF
Predict not taken
X
X
X
But actually taken
X
X
X
So FLUSH 3 instructions

## Slide 18: Why Do We Have to Flush 3 Instructions?
The ZERO output from the ALU, which is used to make the branch selection, is available at the end of the EX stage
It is then pipelined, so the branch decision is made in the ME stage
This means that we load the PC with the target address in the following stage, which is 3 cycles later