## Slide 1: ECEN 3593-001 Computer Organization
Lecture #16
24 February 2021

## Slide 2: Agenda
Class Announcements
Phase 5 Details
Chapter 4

## Slide 3: Class Announcements
Reading for the week
  “Computer Organization and Design, The Hardware / Software Interface, RISC-V edition,” by David Patterson and John Hennessy
    ISBN 978-0-12-812275-4
    Chapter 4, “The Processor”
    pages 236-314 (sections 4.1 thru 4.8)
OH via Zoom 2:00 to 3:00 today https://cuboulder.zoom.us/j/4317981384

## Slide 4: Class Announcements
Phase 5 is available, Target Date Sunday, February 28 at 10:00 PM
1%/day bonus before that, 4%/day penalty after that (Poll)
Phase 6 will be posted by Friday evening
Target Date Sunday, March 7 at 10:00 PM
1%/day bonus before that, 4%/day penalty after

## Slide 5: Codasip – ca_defines.hcodal
Defines Control Signal enums and widths
enum – define names for all possible Control signal values
Can easily add additional values in future Phases
Define the bit width as a function of the number of enums – automatically adjusted if enums added
First enum is assigned 0 – the default value
All Control signals MUST be defined in this way, and the enums MUST be used in the code

## Slide 6: Codasip – ca_resources.codal
Defines all signals used in the design
Signals - [ADDR_W] is the bit width (see share/include/config.hcodal for definitions)
Registers
Must specify the pipeline stage
Control widths like ALUOP_W created in defines.hcodal

## Slide 7: Codasip – ca_resources.codal
MUST have the correct width for every signal
Determining Signal Width
All data path widths are 32 bits
  WORD_W for data signals like s_ex_alu
  ADDR_W for address path signals like r_pc
  INSTR_W for the instruction
If the signal has a bitfield specification, that defines the width
  All necessary widths have constants in config.hcodal except “1”
The width of every register output is the same as the width of its input

## Slide 8: Codasip – ca_decoder.codal
CA Equivalent of isa.codal
element name adds “_hw”
opc_* definitions come from isa.codal
Define the value of every Control signal for this instruction group
Use the enums created in ca_defines.hcodal
Every Control signal must be defined in every group

## Slide 9: Codasip – Multiplexor Example
Schematic of a mux
Codal version 1 – switch statement on the Control signal
Has a CASE for each enum
Default prints an error which helps in debug

## Slide 10: Codasip – Multiplexor Example 2
Alternate mux implementations
if/else instead of switch
If/else for a 1-bit Control signal
?/: statement for a 1-bit Control signal
The last two are much harder to understand and not recommended

## Slide 11: Class Project – Phase 5
Bit Field Syntax
  Double periods indicate a bit range (NOT “:”)
  A 1-bit range must include 2 values (e.g. [7..7])
  Double colons indicate concatenation
  int12 creates a signed 12-bit value
  int32 sign extends the value to 32 bits
This defines the signals which are broken out of the s_id_instr bus on the ID Stage schematic

## Slide 12: Class Project – Phase 5
Accessing the Instruction Memory (IF Stage)
  Address part function
  Defines the address phase (IF Stage schematic)
  Defines the operation (always read for IM)
  Defines the word address
  Defines the byte offset
  Defines the access length (4 bytes here)

## Slide 13: Class Project – Phase 5
Accessing the Instruction Memory (ID Stage)
  Data part function
  Defines the data phase (ID Stage schematic)
  Read output
Handles the -1st instruction
  Force it to be a NOP
  r_id_clear initialized to 1, then set to 0

## Slide 14: More realistic Branch Prediction Methods
Static branch prediction
  Based on typical branch behavior
  Example: assume loop and if-statement branches
    Predict backward branches taken (assume bottom of a loop)
    Predict forward branches not taken (assume IF statement)
Dynamic branch prediction
  Hardware measures actual branch behavior
    e.g., record recent history of each branch
  Assume future behavior will continue the trend
    When wrong, stall while re-fetching, and update history

## Slide 15: How Will We Implement Branch Prediction?
For simplicity, we will implement static prediction but always assume the branch is not taken
What is the penalty for this?
Every branch which is taken, even in a loop, will result in three instructions being FLUSHED

## Slide 16: Pipeline Summary
Pipelining improves performance by increasing instruction throughput
  Executes multiple instructions in parallel
  Each instruction has the same latency
    The instruction latency could be greater than a single-cycle CPU implementation if the stages are non-balanced
Subject to hazards
  Structure, data, control
Instruction set design affects complexity of pipeline implementation