## Slide 1: ECEN 3593-001 Computer Organization
Lecture #17
26 February 2021

## Slide 2: Agenda
Class Announcements
Phase 5
Pipeline continued

## Slide 3: Class Announcements
Reading for the week
  “Computer Organization and Design, The Hardware / Software Interface, RISC-V edition,” by David Patterson and John Hennessy
    ISBN 978-0-12-812275-4
    Chapter 4, “The Processor”
    pages 236-314 (sections 4.1 thru 4.8)

## Slide 4: Class Announcements
Phase 5 is available, Target Date Sunday, February 28 at 10:00 PM
1%/day bonus before that, 4%/day penalty after
Phase 6 is posted
Target Date Sunday, March 7 at 10:00 PM
1%/day bonus before that (maximum 7%), 4%/day penalty after
Separate schematic and Codasip pieces

## Slide 5: Class Announcements
I will have Zoom OH today from 2:00 to 3:00 https://cuboulder.zoom.us/j/4317981384

## Slide 6: Processor Overall Functional View
Register File (Write)
Instruction Memory
Data Memory
Combinational Logic
IN ORDER
r_wb_xx
r_me_xx
r_ex_xx
r_id_xx
Register File (Read)
s_ex_xx
s_wb_xx
s_id_xx
s_STG_xx
clock
New r_*
Comb. Logic
New r_*
May be r_STG_xx
r_pc
All registers are updated SIMULTANEOUSLY

## Slide 7: Class Project – Phase 5
Where is the Pipeline Register of the Instruction?
Normally on the IM output
Inside the MemData block
This is the internal implementation, but the memory has 0 delay in this case.
The output must be a signal because the register is implied in the memory block

## Slide 8: Class Project – Phase 5
Forward References
This is correct

## Slide 9: Class Project – Phase 5
Forward References
This is incorrect – it is a FORWARD REFERENCE
Because the Codasip code is executed in order
Important when setting hardware breakpoints

## Slide 10: Class Project – Phase 5
Flow of a Stage
Each stage has the event STG_output, which must be “used” before it is called
All the code of the stage goes here EXCEPT for the register updates
Then STG_output is called
The register updates go here
Example – r_wb_pc = r_me_pc;

## Slide 11: CLASS Project – Phase 5
Register File Implementation
rf_xpr is a 32 x 32-bit array which holds the 32 registers of the Register File
Read (in ID) accesses the selected register indexed by rs1 and rs2
Write (in WB) loads the selected register based on rd
Diagnostic print statement based on “info”
s_id_reg1 != s_id_rs1

## Slide 12: Class Project – Phase 5
Debugging with “- -info”
In Run -> Debug Configurations, can set this in the Arguments tab
Set the “verbosity” level
Can have multiple “verbosity” levels set, e.g. - -info 3,6,7 (no spaces)
Each level prints diagnostic information just before the clock
  3 – prints register file writes
  6 – prints pipeline instructions
  7 – prints ALU inputs/outputs

## Slide 13: Class Project - -info 3,6,7 Display
Display in console on each cycle
  RF Write – 3
  Pipeline Display – 6
  Current PC
  Instruction in hex
  ALU Display – 7
See the document in the Debug section of Canvas for a complete description

## Slide 14: Codasip Debugging – Debug Perspective
Registers, etc.
Code
Disassembly
Console

## Slide 15: Console Switching
Red error message pops up in Console and then disappears – why?
There are 6 different consoles, selected by the pulldown of the little monitor
  gdb (7.4.1) – the Console of the simulator - used in the Debug Perspective
    The Red error occurs here
  phaseX_test.xexe – outputs from the program - used in the Debug Perspective
    But we switch to this instantly
  Various build consoles – used in the Codasip Perspective
Codasip will switch consoles unexpectedly
The active console is in the upper left corner
To see the error, switch back to the gdb (7.4.1) Console

## Slide 16: Class Project – Phase 5
Observing signals
  Set a HW Breakpoint
  Hover over a signal with the mouse
  A display of the signal value pops up
  You can quickly step through signals
  Can only look before the BP, after the code has been executed. This BP is too early

## Slide 17: Microarchitectural Register Display

## Slide 18: Signal Display

## Slide 19: Breakpoints Display

## Slide 20: Class Project – Phase 5
Codasip Helps with Debug
  Black text => missing
  ? => Syntax error
  Error message often gives error code (click to go to Help)
  Error message often gives the correct error location (click to go there)