## Slide 1: ECEN 3593-001 Computer Organization
Lecture #19
3 March 2021

## Slide 2: Agenda
Class Announcements
Chapter 4 - Hazards

## Slide 3: Class Announcements
Reading for the week
  “Computer Organization and Design, The Hardware / Software Interface, RISC-V edition,” by David Patterson and John Hennessy
    ISBN 978-0-12-812275-4
    Chapter 4, “The Processor”
Phase 5 is in the 4%/day penalty stage (12% today)
Phase 6 Target Date Sunday, March 7 at 10:00 PM
Zoom Office Hours 2:00 to 3:00 today https://cuboulder.zoom.us/j/4317981384

## Slide 4: Class Announcements
The Midterm Exam will be on Wednesday, March 17 in class
Homework #3 is posted
Due Tuesday, March 9 at 10:00 PM

## Slide 5: Phase 6 Scoring
Schematic is 20% of total, Project is 80% of total
Schematic deductions the same as Phase 4, and are from the total score (not just the 20%)
Schematic – 1% bonus points per day before Target Date, maximum of 7% (all of the 20% schematic total)
Submit schematic early to get it reviewed
Project – 1% bonus points per day before Target Date
Both – 4% per day penalty after Target Date

## Slide 6: Data Forwarding
sub x2, x1, x3
IM
RF
DM
RF
and x12, x2, x5
IM
RF
DM
RF
or x13, x6, x2
IM
RF
DM
RF
add x14, x2, x2
IM
RF
DM
RF
sd x15, 100(x2)
IM
RF
DM
RF
Clock Cycle
CC0
CC1
CC2
CC3
CC4
CC5
CC6
CC7
CC8

## Slide 7: Detecting the need to forward
Pass register indices along pipeline
  e.g., ID/EX.RegisterRs1 = register index for Rs1 sitting in ID/EX pipeline register
ALU operand register numbers in EX stage are given by
  ID/EX.RegisterRs1, ID/EX.RegisterRs2 (r_ex_rs1 and r_ex_rs2)

## Slide 8: Pipeline Control
Pass necessary information down the pipeline
Note that rd is already passed down the pipeline

## Slide 9: Detecting the need to forward
Pass register numbers along pipeline
  e.g., ID/EX.RegisterRs1 = register number for Rs1 sitting in ID/EX pipeline register
ALU operand register numbers in EX stage are given by
  ID/EX.RegisterRs1, ID/EX.RegisterRs2 (r_ex_rs1 and r_ex_rs2)
Data hazards when
  1a. EX/MEM.RegisterRd (r_me_rd) = ID/EX.RegisterRs1
  1b. EX/MEM.RegisterRd (r_me_rd) = ID/EX.RegisterRs2
  2a. MEM/WB.RegisterRd (r_wb_rd) = ID/EX.RegisterRs1
  2b. MEM/WB.RegisterRd (r_wb_rd) = ID/EX.RegisterRs2
Fwd from ME pipeline reg
Fwd from WB pipeline reg

## Slide 10: Detecting the need to forward
But only if forwarding instruction will write to a register!
  EX/MEM.RegWrite, MEM/WB.RegWrite = 1
And only if Rd for that instruction is not x0
  EX/MEM.RegisterRd ≠ 0, MEM/WB.RegisterRd ≠ 0

## Slide 11: Forwarding paths
Mux on src1 side of ALU
Mux on src2 side of ALU
Forwarding control logic

## Slide 12: Forwarding conditions

## Slide 13: Double Data Hazard
Consider the sequence:
  add x1,x1,x2 add x1,x1,x3 add x1,x1,x4
Both hazards occur
  Want to use the most recent
Revise MEM/WB hazard condition
  Only forward if EX/MEM hazard condition isn’t true
x1 forwarded from the EX/MEM register
x1 forwarded from the EX/MEM register, not from the MEM/WB register

## Slide 14: Revised Forwarding condition
MEM hazard
  if (MEM/WB.RegWrite
  and (MEM/WB.RegisterRd ≠ 0)
  and not(EX/MEM.RegWrite and (EX/MEM.RegisterRd ≠ 0)
  and (EX/MEM.RegisterRd = ID/EX.RegisterRs1))
  and (MEM/WB.RegisterRd = ID/EX.RegisterRs1)) ForwardA = 01
  if (MEM/WB.RegWrite
  and (MEM/WB.RegisterRd ≠ 0)
  and not(EX/MEM.RegWrite and (EX/MEM.RegisterRd ≠ 0)
  and (EX/MEM.RegisterRd = ID/EX.RegisterRs2))
  and (MEM/WB.RegisterRd = ID/EX.RegisterRs2)) ForwardB = 01

## Slide 15: Forwarding paths

## Slide 16: Load Data Hazard
ld x12, 100(x3)
IM
RF
DM
RF
add x1, x12, x2
IM
RF
DM
RF
IM
RF
DM
RF
IM
RF
DM
RF
IM
RF
DM
RF
Clock Cycle
CC0
CC1
CC2
CC3
CC4
CC5
CC6
CC7
CC8
nop
stall
add x1, x12, x2
What type of forwarding is then used here? (Poll)
MEMWB

## Slide 17: Load-Hazard Detection
Check when using instruction is decoded in ID stage
ALU operand register numbers in ID stage are given by
  IF/ID.RegisterRs1, IF/ID.RegisterRs2 (s_id_rs1, s_id_rs2)
Load-use hazard when
  ID/EX.MemRead and ((ID/EX.RegisterRd (r_ex_rd) = IF/ID.RegisterRs1) or (ID/EX.RegisterRd (r_ex_rd) = IF/ID.RegisterRs2))
If detected, stall and insert bubble

## Slide 18: How to insert a bubble and stall the pipeline
Force control values in ID/EX register to 0
  EX forced to a NOP (no-operation)
Inserting a “bubble” in EX

## Slide 19: Data path with hazard detection

## Slide 20: Inserting a bubble
Force control values in ID/EX register to 0
  EX forced to a NOP (no-operation)
  In Codasip we do this by asserting s_ex_clear
  0 for branch control will disable the branch AND gate
  0 for MemRead will disable load operation
  0 for MemWrite will disable store operation
  0 for RegWrite will prevent an update to the Register file
This is why the first enum in Codasip must be NOP

## Slide 21: How to insert a bubble and stall the pipeline
Force control values in ID/EX register to 0
  EX forced to a NOP(no-operation)
Prevent update of PC and IF/ID register
  Using instruction is decoded again
  Following instruction is fetched again
  1-cycle stall allows MEM to read data for ld
    Can subsequently transfer to EX stage
Inserting a “bubble”
Stalling the pipeline before the decode stage

## Slide 22: Load Hazard Pipeline Flow
IF
ID
EX
ME
WB
ld x1, -20(x2)
add x2, x1, x3
ld
ld
add
ld
add
hazard
pc-1
pc-2
pc-3
pc-4
pc-1
pc-2
pc-3
pc-1
pc-2
pc+1
stall
add
pc+1
ld
pc-1
nop
MEMWB forwarding
bubble
Clock 1
Clock 2
Clock 3
Clock 4
pc+1
pc+2
ld
nop
Clock 5
add
proceed