## Slide 1: ECEN 3593-001 Computer Organization
Lecture #21
8 March 2021

## Slide 2: Agenda
Class Announcements
Finish Chapter 4
Chapter 1

## Slide 3: Class Announcements
Reading Assignment
  “Computer Organization and Design, The Hardware / Software Interface, RISC-V edition,” by David Patterson and John Hennessy
    ISBN 978-0-12-812275-4
    Chapter 1, “Computer Abstractions and Technology”
      Sections 1.1 thru 1.11 required
      Section 1.12 (optional)
    pages 2-54
Homework #3 is due on Tuesday, March 9 at 10:00 PM

## Slide 4: Class Announcements
Phase 6 is in the deduction period – 4%/day
Phase 7 is posted – Target Date Sunday, March 21 at 10:00 PM
Bonus 1%/day (maximum 7%)
Deduction 4%/day

## Slide 5: Mid-Term
Mid-Term will be held in class on Wednesday, March 17
Mid-Term practice exam will be posted by Thursday
“Computer Organization and Design” text book, and RISC-V ISA specifications will be required for reference for figures as well as to create and decode RISC-V machine code
The Mid-Term will be taken through a Canvas quiz
  50 minutes
  1 attempt
  Open Book, but not Open People, and not google

## Slide 6: Mid-Term
Mid-Term compensation
  4 questions similar to questions in homework #1 thru #3
    Quiz bank of 12-18 questions
    (estimating 30 minutes)
    ~50% of Mid-Term
  15 multiple choice / matching questions
    Quiz bank of 30-45 questions
    Definitions / Theory based questions to test comprehension of the course material
    (estimating 15 minutes)
    ~50% of Mid-Term
Suggestion: If you are stuck on a problem, make note of it and move on to complete other questions. Then go back and work on the problems that you passed over the first time
  Do not lose the opportunity to complete questions that you know

## Slide 7: RISC-V Cores are Proliferating

## Slide 8: Current Branch implementation
Create condition
Create the target address
Determine whether to branch
Select the branch target address

## Slide 9: Branch Hazards - If branch outcome determined in MEM
Flush these instructions
(Set s_STG_clear values to 1)
The zero bit is available to enable the “AND” gate (branch function) to PC branch multiplexor
PC
The hazard that is the result of determining the proper instruction to fetch is called a control or branch hazard
32

## Slide 10: Can We Accelerate Jumps?
Why could this be faster than a conditional branch?
Can assert the PC mux control in the ID stage (why?)
We don’t need to wait for the condition out of the ALU
We have the PC and the jump offset in the ID stage (why?)
Jump Target Address needs only the PC and the immediate
How many instructions need to be flushed in this case?
1, because we still need an extra cycle to compute the target address

## Slide 11: Accelerating JAL
Move adder to ID
Don’t pipeline result
Decode PCSrc directly from the instruction
Why doesn’t this work for JALR?
Need the ALU output as the branch address

## Slide 12: Dynamic Branch Prediction
In deeper and superscalar pipelines, branch penalty is more significant
Use dynamic prediction – prediction of branches at runtime using runtime information
  Branch prediction buffer (aka branch history table)
  Indexed by recent branch instruction addresses
  Stores outcome (taken/not taken)
  To execute a branch
    Check table, expect the same outcome
    Start fetching from fall-through or target
    If wrong, flush pipeline and flip prediction

## Slide 13: Dynamic Branch Prediction Buffer
Branch Prediction Buffer or Branch History Buffer is a small memory that is indexed by the lower portion of the address of the branch instruction and contains one or more bits indicating whether the branch was recently taken
An example of a 256 entry branch prediction buffer
If incorrect prediction, the CPU must flush the incorrect instruction fetched
Bits indicating branch taken or not
Branch PC address lower 8 bits [9:2] ->
Branch previously taken
If “taken,” use branch target address, if not taken, use PC+4

## Slide 14: 1-Bit Predictor: Shortcoming
Inner loop branches miss predicted twice
Miss predict as taken on last iteration of inner loop
Then miss predict as not taken on first iteration of inner loop next time around
outer: … … inner: …
…
beq …, …, inner … beq …, …, outer

## Slide 15: 2-bit Branch predictors
Only change prediction on two successive mispredictions

## Slide 16: Calculating the Branch target address
Even with predictor, still need to calculate the target address
  1-cycle penalty for a taken branch
Branch target buffer
  Cache of target addresses
  Indexed by PC when instruction fetched
    If hit and instruction is branch predicted taken, can fetch target immediately

## Slide 17: Branch Target Buffer
An example of a 256 entry branch prediction buffer
Branch Prediction Buffer a structure that caches the destination instruction for a branch
Need a “Tag” memory to hold upper address
Previous stored upper 22-bits of last branch taken at this address
Bits indicating branch taken or not
Branch PC address lower 8 bits ->
Branch PC address upper 22 bits
22-bit comparator
1 = Entry is in Branch Prediction Buffer
Branch previously taken
If “taken,” use branch target address, if not taken, use PC+4
Branch target address

## Slide 18: Chapter 4 Summary
RISC-V is architected specifically to optimize a pipelined design
The hardware architecture is heavily influenced by the ISA

## Slide 19: What is Performance?
Computer designers goals
  Minimize execution time
  Minimize development cost and sale price
How to minimize execution time?
  Improve the technology of the components
  Minimize clock cycles per instruction
  Improve instruction efficiency
=

## Slide 20: Fundamental Performance Rule
The ONLY VALID MEASURE of performance is EXECUTION TIME

## Slide 21: Definitions
Harvard architectures
  Processors that have separate instruction and data caches, but more importantly, separate instruction and data busses
  What advantage does this provide?
    Parallel access to instructions and data
Von Neumann architectures
  Instruction and data memories share a bus
  Resource conflict, the memory bus
    Limits performance
  Fewer interconnections required
https://en.wikipedia.org/wiki/Von_Neumann_architecture
https://en.wikipedia.org/wiki/Harvard_architecture
Minimizes
Performance via Parallelism