## Slide 1: ECEN 3593-001 Computer Organization
Lecture #29
29 March 2021

## Slide 2: Agenda
Class Announcements
Class Project
Finish Chapter 4

## Slide 3: Class Announcements
Reading assignment for the week
  “Computer Organization and Design, The Hardware / Software Interface, RISC-V edition,” by David Patterson and John Hennessy
    ISBN 978-0-12-812275-4
    Chapter 5, “Large and Fast: Exploiting Memory Hierarchy”
    pages 364-410 (sections 5.1 thru 5.4)
My OH on Zoom today 2:00 to 3:00 https://cuboulder.zoom.us/j/4317981384

## Slide 4: Class Announcements
Phases 5 and 6 are in the deduction period – 1%/day
Phase 7 is in the deduction period – 4%/day
Phase 8 is posted
Target Date Sunday, April 4 at 10:00 PM
Bonus 1%/day, deduction 4%/day
Homework #4 is due Thursday, April 1 at 10:00 PM

## Slide 5: Homework #4 Typos
Question 3 – Instruction Class C is 40% of the instructions, not 30%
  Total must add to 100%
Question 5 – In the third part, the “40% increase” should be 30% to match the previous sentence.

## Slide 6: Definitions
Imprecise Interrupt or Imprecise Exception: Interrupts or exceptions in pipelined computers that are not associated with an exact instruction that was the cause of the interrupt or exception
  Leaves it up to the operating system to determine which instruction caused the problem
Precise Interrupt or Precise Exception: An interrupt or exception that is always associated with the correct instruction in pipelined computers

## Slide 7: Imprecise exceptions
Just stop pipeline and save state
  Including exception cause(s)
Let the handler work out
  Which instruction(s) had exceptions
  Which to complete or flush
    May require “manual” completion
Simplifies hardware, but more complex handler software
  Not feasible for complex multiple-issue out-of-order pipelines to be decided by software

## Slide 8: Precise exceptions
Causing instruction is known
All instructions in front of the exception instruction can be allowed to complete
Any instructions after the exception instruction in an out of order CPU must be voided/flushed
With the advent of out of order instructions to increase performance, precise exception based CPUs are becoming the norm

## Slide 9: Instruction Level Parallelism (ILP)
Pipelining: executing multiple instructions in parallel
To increase ILP
  Deeper pipeline (more stages)
    Less work per stage  shorter clock cycle
  Multiple issue
    Replicate pipeline stages  multiple pipelines
    Start multiple instructions per clock cycle
    CPI < 1, so sometimes use Instructions Per Cycle (IPC)
    E.g., 4GHz 4-way multiple-issue
      16 BIPS, peak CPI = 0.25, peak IPC = 4
    But dependencies reduce this in practice

## Slide 10: Definitions
Instruction-Level Parallelism (ILP): Parallelism among instructions
  It can be due to a pipeline where one instruction pipeline stage executes in parallel with another instruction in a different stage
  Multiple simultaneous pipelines running together
Multiple Issue: A scheme whereby multiple instructions are launched in one clock cycle
Static Multiple Issue: An approach to implementing a multiple-issue processor where many decisions are made by the compiler before execution
Dynamic Multiple Issue: An approach to implementing a multiple issue processor where many decisions are made during execution by the processor

## Slide 11: Definitions
Issue slots: The positions from which the instructions could issue in a given clock cycle
  The slots at the beginning of a pipeline
Speculation: An approach whereby the compiler or processor guesses the outcome of an instruction to remove it as a dependence in executing other instructions
  Branch prediction is an example of speculation
Issue packet: The set of instructions that issue together in one clock cycle; the packet may be determined statically by the compiler or dynamically by the processor
Very Long Instruction Word (VLIW): A style of instruction set architecture that launches many operations that are defined to be independent in a single wide instruction

## Slide 12: Multiple Issue
Static multiple issue
  Compiler groups instructions to be issued together
  Packages them into “issue slots”
  Compiler detects and avoids hazards
Dynamic multiple issue
  CPU examines instruction stream and chooses instructions to issue each cycle
  Compiler can help by reordering instructions
  CPU resolves hazards using advanced techniques at runtime

## Slide 13: Static Multiple Issue RISC-V example
In a 2 issue slot static multiple issue processor, the compiler organizes pairs of instructions to be on a 64-bit, 2 word boundaries
  The instructions must not be dependent on each other
  Reorder instructions to remove or minimize dependencies
  If the instructions must be dependent on each other, the later instruction is moved to the next 64-bit boundary an a NOP is inserting in its place
  Increase performance at the expense of memory due to the introduction of NOPs

## Slide 14: RISC-V with static dual issue
Two-issue packets
  One ALU/branch instruction
  One load/store instruction
  64-bit aligned
    ALU/branch, then load/store
    Pad an unused instruction with nop

## Slide 15: RISC-V with Static dual issue
Fetch 2 instructions
Must add 8
ALU data path
Replicate RF access (R/W)
Load/store data path
8

## Slide 16: Hazards in the dual issue RISC-V
More instructions executing in parallel
EX data hazard
  Forwarding avoided stalls with single-issue
  Now can’t use ALU result in load/store in same packet
    add x10, x0, x1 load x2, 0(x10)
    Split into two packets, effectively a stall
Load-use hazard
  Still one cycle use latency, but now two instructions
More aggressive scheduling (in the Compiler) required
Must schedule no data dependency instruction between the add and load
Use latency: Number of clock cycles between a load instruction and an instruction that can use the result of the load without stalling the pipeline

## Slide 17: Chapter 4
You now know how to design a full RISC-V processor !!

## Slide 18: Chapter 5
Large and Fast:
Exploiting Memory Hierarchy

## Slide 19: Principle of Locality
Programs access a small proportion of their address space at any time
Temporal locality
  Items accessed recently are likely to be accessed again soon
  e.g., instructions in a loop, loop variables
Spatial locality
  Items near those accessed recently are likely to be accessed soon
  E.g., sequential instruction access, array data

## Slide 20: Taking Advantage of Locality
Memory hierarchy
Store everything on disk
Copy recently accessed (and nearby) items from disk to smaller, faster DRAM memory
  Main memory
Copy more recently accessed (and nearby) items from DRAM to smaller, faster SRAM memory
  Cache memory attached to CPU
Design Principle – Smaller is Faster

## Slide 21: Memory Hierarchy Levels
Block (aka line): unit of copying
  May be multiple words
If accessed data is present in upper level
  HIT: access satisfied by upper level
    Hit ratio: hits/accesses
If accessed data is absent
  MISS: block copied from lower level
    Time taken: miss penalty
    Miss ratio: misses/accesses = 1 – hit ratio
  Then accessed data supplied from upper level

## Slide 22: Memory Technology
Static RAM (SRAM)
  0.5ns – 2.5ns, $2000 – $5000 per GB
Dynamic RAM (DRAM)
  50ns – 70ns, $20 – $75 per GB
Magnetic disk
  5ms – 20ms, $0.20 – $2 per GB
Ideal memory
  Access time of SRAM
  Capacity and cost/GB of disk
Cost is inversely proportional to access time. As access time becomes greater, the cost per GB goes down