## Slide 1: ECEN 3593-001 Computer Organization
Lecture #32
5 April 2021

## Slide 2: Agenda
Class Announcements
Course Project discussion
Chapter 5 – Major Cache Description

## Slide 3: Our class as Freshmen??

## Slide 4: Class Announcements
Reading assignment for the week
  “Computer Organization and Design, The Hardware / Software Interface, RISC-V edition,” by David Patterson and John Hennessy
    ISBN 978-0-12-812275-4
    Chapter 5, “Large and Fast: Exploiting Memory Hierarchy”
    pages 364-415 (sections 5.1 thru 5.5)
    NOTE: This adds section 5.5 which is related to Phase 9
My OH today 2:00 to 3:00 on Zoom - https://cuboulder.zoom.us/j/4317981384

## Slide 5: Class Announcements
Phases 5/6/7 are in the deduction period – 1%/day
Phase 8 is in the deduction period – 4%/day
Phase 9 is posted – Target Date Sunday, April 11 at 10:00 PM
Bonus 1%/day (maximum 7%), Deduction 4%/day
Homework #4 due tonight at 10:00 PM
Homework #5 will be posted next week and due early the following week

## Slide 6: Phase 8
Use the key available resources
  Slides 6 through 15 of Lecture 28
  MEMCTL Design document in Canvas
  Section 4.7 of the textbook for Load Hazards
Use - -info 8,9,10 to see the operation of MEMCTL and the memory block
Use - -info 6 to see the stall/clear behavior
  Stalls due to MEMCTL – IF/ID/EX, 4 per operation
  Load hazard – stall IF/ID, clear EX to insert the bubble
Verify store in a Memory Monitor – make sure you have the right Rendering (standardname8 as_data)

## Slide 7: Phase 8
Questions???

## Slide 8: Cache So Far (Read)
Main Memory
Cache/Memory consist of Lines/Blocks
Address comes from the processor
Four Fields in the address
  Byte offset – select byte
  Block offset – select word
  Index – select Cache line
  Upper Address - remainder
Need to know two key things on an access:
  Is the data in the Cache?
  If so, where is it?
Add a Tag to each cache block
Select the Tag with the Index
Compare to the Upper Address
HIT if a match
MISS if no match
If HIT, data is in this Cache line
…
Cache
Word A
Off
Ind
Upper
Address
Block/Line
B
Select Block
Tag
Select Block/Tag
Tag
Tag
Tag
Tag
Tag
Tag
Tag
Cmpr
Hit
MUX
Read Data
Block/Line
Word A
MUX

## Slide 9: Initialization
MISS
Main Memory
How do we handle startup?
All Tags are initially invalid – no data in the Cache
Add a Valid bit to each Tag
  All initially clear
If Valid bit is clear, force a MISS
Set the Valid bit when line is written
…
Cache
Word A
Off
Ind
Upper
Address
Block/Line
B
Select Block
Tag
Select Block/Tag
Tag
Tag
Tag
Tag
Tag
Tag
Tag
Cmpr
HIT
MUX
Read Data
Block/Line
Word A
MUX
V
V
V
V
V
V
V
V
V

## Slide 10: What Happens on a Miss?
Main Memory
…
Cache
Word A
Off
Ind
Upper
Address
Block/Line
B
Select Block
Tag
Select Block/Tag
Tag
Tag
Tag
Tag
Tag
Tag
Tag
Cmpr
MISS
MUX
Read Data
Block/Line
Word A
MUX
V
V
V
V
V
V
V
V
Stall the Processor
Initiate a Memory read of the block containing the addressed word
Load that data into the indexed block of the cache
Update the Tag from the Upper Address field
Finish the cache read as a hit
Select Block
Read Data
Tag
HIT

## Slide 11: Cache Misses
On cache hit, CPU proceeds normally
On cache miss
  Stall the CPU pipeline
  Fetch block from next level of hierarchy
    Update the Tag -> Now get a HIT
  Instruction cache miss
    Restart instruction fetch
  Data cache miss
    Complete data access
Cache miss: a request for data from the cache that cannot be filled because the data is not present in the cache

## Slide 12: Instruction cache miss steps
Note: The instruction address of the Cache is actually the PC
Halt the processor in an In-Order CPU
Send the original PC value (current PC) to the next lower level of memory
Write the entry into cache, put the data from the memory in the data portion of the cache, the upper address bits into the tag field, and set the valid bit to true
Restart the instruction execution at the first step, fetching the instruction, but this time, it will have a cache hit in the instruction cache

## Slide 13: What Happens on a Write Hit?
Main Memory
…
Cache
Word A
Off
Ind
Upper
Address
Block/Line
B
Select Block
Tag
Select Block/Tag
Tag
Tag
Tag
Tag
Tag
Tag
Tag
Cmpr
Hit
MUX
Read Data
Block/Line
Word B
MUX
V
V
V
V
V
V
V
V
Write the data to the cache
  NOTE – cache line no longer matches the Main Memory line
Then – depends on the cache type
  WRITETHROUGH – copy the line from the cache to Main Memory – Cache matches Main Memory again
Word B

## Slide 14: What Happens on a Write Hit?
Main Memory
…
Cache
Word A
Off
Ind
Upper
Address
Block/Line
B
Select Block
Tag
Select Block/Tag
Tag
Tag
Tag
Tag
Tag
Tag
Tag
Cmpr
Hit
MUX
Read Data
Block/Line
Word B
MUX
V
V
V
V
V
V
V
V
Write the data to the cache
  NOTE – cache line no longer matches the Main Memory line
Then – depends on the cache type
  WRITETHROUGH – copy the line from the cache to Main Memory – Cache matches Main Memory again
  WRITEBACK – set a Dirty bit in the Tag Memory – Cache now different from Main Memory
    We will need to handle this in a later reference
D
D
D
D
D
D
D
D

## Slide 15: Writethrough Cache
Writethrough: update memory on each write
But makes writes take longer
  e.g., if base CPI = 1, 10% of instructions are stores, write to memory takes 100 cycles
    Effective CPI = 1 + 0.1×100 = 11
Solution A: write only the modified word to Memory
  No help if cache <-> memory path is a line wide
Solution B: write buffer
  FIFO which holds data waiting to be written to memory
Write through: a scheme in which writes always update both the cache and the next lower level of memory hierarchy, ensuring that data is always consistent between the two levels of memory

## Slide 16: Write Buffer on a Writethrough Cache
Main Memory
…
Cache
Word A
Off
Ind
Upper
Address
B
Select Block
Tag
Select Block/Tag
Tag
Tag
Tag
Tag
Tag
Tag
Tag
Cmpr
Hit
MUX
Read Data
Block/Line
Word B
MUX
V
V
V
V
V
V
V
V
Write data to Write Buffer immediately
Remove stall so processor can proceed
Then copy to Main Memory
Write Buffer

## Slide 17: Writethrough Cache
Writethrough: update memory on each write
But makes writes take longer
  e.g., if base CPI = 1, 10% of instructions are stores, write to memory takes 100 cycles
    Effective CPI = 1 + 0.1×100 = 11
Solution A: write only the modified word
  No help if cache <-> memory path is a line wide
Solution: write buffer
  FIFO which holds data waiting to be written to memory
  CPU continues immediately
    Only stalls on write if write buffer is already full
Write through: a scheme in which writes always update both the cache and the next lower level of memory hierarchy, ensuring that data is always consistent between the two levels of memory
Write buffer: a queue that holds the data while the data is waiting to be written to memory
Note: if the write buffer is full when the processor reaches a write, the processor must stall until there is an empty position in the queue

## Slide 18: What Happens on a Dirty Write Miss?
Main Memory
…
Cache
Word A
Off
Ind
Upper
Address
Block/Line
B
Select Block
Tag
Select Block/Tag
Tag
Tag
Tag
Tag
Tag
Tag
Tag
Cmpr
MISS
MUX
Read Data
Block/Line
Word B
MUX
V
V
V
V
V
V
V
V
Cannot write the data to the cache
  Cache line is Dirty
  Stall the processor
Copy the Dirty line to Main Memory
  Use Tag as Upper Address
Copy the addressed line from Main Memory to the Cache
Update the Tag with the Upper Address
Clear the Dirty bit
Now we will have a HIT
Write the new data
  Set the Dirty Bit
Remove the processor stall
D
D
D
D
D
D
D
D
Word A
D
Word B
Word B
Word C
Tag
HIT

## Slide 19: What Happens on a Dirty Read Miss?
Main Memory
…
Cache
Word A
Off
Ind
Upper
Address
Block/Line
B
Select Block
Tag
Select Block/Tag
Tag
Tag
Tag
Tag
Tag
Tag
Tag
Cmpr
MISS
MUX
Read Data
Block/Line
Word B
MUX
V
V
V
V
V
V
V
V
Cannot read the data from the cache
  Cache line is Dirty
  Stall the processor
Copy the Dirty line to Main Memory
  Use Tag as Upper Address
Copy the addressed line from Main Memory to the Cache
Update the Tag with the Upper Address
Clear the Dirty bit
Now we will have a HIT
Read the new data
Remove the processor stall
D
D
D
D
D
D
D
D
Word A
D
Word B
Word B
Tag
HIT
Read Data

## Slide 20: Next lecture
Details of Error Correcting Codes (ECC) which is the key element in Phase 9