## Slide 1: ECEN 3593-001 Computer Organization
Lecture #33
7 April 2021

## Slide 2: Agenda
Class Announcements
Chapter 5
ECC and Phase 9

## Slide 3: Class Announcements
Reading assignment for the week
  “Computer Organization and Design, The Hardware / Software Interface, RISC-V edition,” by David Patterson and John Hennessy
    ISBN 978-0-12-812275-4
    Chapter 5, “Large and Fast: Exploiting Memory Hierarchy”
    pages 410-449 (sections 5.5 thru 5.8)
OH today 2:00 to 3:00 if I get a request before 2:00

## Slide 4: Class Announcements
Phases 5/6/7 are in the deduction period – 1%/day
Phase 8 is in the deduction period – 4%/day
Phase 9 is posted – Target Date Sunday, April 11 at 10:00 PM
Bonus 1%/day (maximum 7%), Deduction 4%/day
Homework #4 will be graded by Friday
Homework #5 will be posted next week and due early the following week

## Slide 5: Final Exam
May 3, 1:30 to 4:00 PM, Online
~20 Homework style questions
~30 short questions
Twice as many questions as the MidTerm, but 3 times as much time
The Final Exam is typically quite challenging

## Slide 6: Phase 8
Use the key available resources
  Slides 6 through 15 of Lecture 28
  MEMCTL Design document in Canvas
  Section 4.7 of the textbook for Load Hazards
Use - -info 8,9,10 to see the operation of MEMCTL and the memory block
Use - -info 6 to see the stall/clear behavior
  Stalls due to MEMCTL – IF/ID/EX, 4 per operation
  Load hazard – stall IF/ID, clear EX to insert the bubble
Verify store in a Memory Monitor – make sure you have the right Rendering (standardname8 as_data)

## Slide 7: Class project Phase 8
Questions???

## Slide 8: What is ECC?
Error Correcting Code
Include additional bits in each memory location
Generate them with a specific algorithm, similar to parity
Can then use them to check every bit for errors
Invert any bit which is incorrect
With > log2(bits), can correct any single error
With 1 additional bit, can detect any double error
Textbook and Wikipedia have 8-bit data examples

## Slide 9: ECC Implementation
Memory (64 bits)
Write Data
ECC (7 bits)
D
ECC Generate
ECC Check
Error Encode
XOR
Read Data
We will use a Hamming Code
On write, generate ECC parity bits from Write Data (example is 64-bit data width)
Each is parity across a subset of the bits
On read, check parity for each subset – creates the check bits (together the Syndrome)
Encode the result into 64 bits
XOR the encoded value with the read data from Memory
Result is the correct data IF:
  At most 1 error occurred
If 2+ errors, may or may not get error signal
Add 1 more bit, can detect all 2-bit errors
How many total bits are necessary? (Poll)
Error

## Slide 10: Generating the ECC Code
This is a Hamming Code, based on parity
Bit positions of 22-bit data to be processed
Create each parity bit as the parity of all bits with X’s in its row except itself
Add the parity bits as bits [21:16] of the data word
  p1 = bit 16, p32 = bit 21
p1 = d0 ^ d1 ^ d3 ^ d4 ^ d6 ^ d8 ^ d10 ^ d11 ^ d13 ^ d15

## Slide 11: Checking the ECC Code
Compute the parity of each group including the pX bit – these are the check bits
Create a Syndrome of the check bits
If Syndrome = 0, no errors
Find the column with the matching Syndrome
Invert the data bit of the matching column
No match to Syndrome => uncorrectable
c1 = d0 ^ d1 ^ d3 ^ d4 ^ d6 ^ d8 ^ d10 ^ d11 ^ d13 ^ d15 ^ p1
Syndrome = c32 :: c16 :: c8 :: c4 :: c2 :: c1
33
34
35
53
32

## Slide 12: Phase 9 – How Does SEC Actually Work?
If any bit gets an error (i.e. is inverted), every Check bit with an X in that column will be inverted (i.e. become a 1 in the Syndrome)
Assume an error in bit d4 (Poll)
Check bits p1, p8 and p32 will be inverted => Syndrome = 101001 = 41
Thus Syndrome = 41 => Data bit d4 had the error
Generate the Parity Bits as XORs of the other bits in the row in the Encoder
If no errors, in Decoder Check Bit = pX ^ pX = 0

## Slide 13: Phase 9 – How Does DED Work?
If the Check bit p32 is a 0, an even number of errors has occurred (0, 2, 4, etc.)
If all other Check bits are 0 (Syndrome = 0) assume no errors
Otherwise, we know that at least two errors occurred
If the Check bit p32 is a 1, an odd number of errors has occurred (1, 3, 5, etc.)
If Syndrome match, assume one error