## Slide 1: ECEN 3593-001 Computer Organization
Lecture #34
9 April 2021

## Slide 2: Agenda
Class Announcements
Course Project discussion – Phase 9
Chapter 5

## Slide 3: Class Announcements
Reading assignment for the week
  “Computer Organization and Design, The Hardware / Software Interface, RISC-V edition,” by David Patterson and John Hennessy
    ISBN 978-0-12-812275-4
    Chapter 5, “Large and Fast: Exploiting Memory Hierarchy”
    pages 410-449 (sections 5.5 thru 5.8)
OH today 2:00 to 3:00 in Zoom - https://cuboulder.zoom.us/j/4317981384

## Slide 4: Class Announcements
Phase 7 is in the deduction period – 1%/day
Phase 8 is in the deduction period – 1%/day (new scoring)
Phase 9 is posted – Target Date Sunday, April 11 at 10:00 PM
Phase 10 will be posted by Sunday
Target Date Sunday, April 18 at 10:00 PM
Bonus 1%/day, Deduction 4%/day

## Slide 5: Class Announcements
Homework #5 will be posted early next week and due the following week
Homework #4 grades have been corrected
Homework #4 Solution Guide posted in Canvas

## Slide 6: Final Exam
May 3, 1:30 to 4:00 PM, Online
~20 Homework style questions
~30 short questions
Twice as many questions as the MidTerm, but 3 times as much time
The Final Exam is typically quite challenging
There will be a Practice Final available the week before the real Final

## Slide 7: ECC Calculation
Data in = 0x1256
Convert to binary (bits in reverse)
Get p1 1’s (Poll)
Count (3)
odd -> 1 even -> 0
p1 = 1
6 5 2 1
0 1 1 0 1 0 1 0 0 1 0 0 1 0 0 0
p2(4) = 0
p4(3) = 1
p8(3) = 1
p16(1) = 1

## Slide 8: ECC Calculation for p32
Include parity bits p1 through p16
Count 1’s for p32
9 => p32 = 1 – why?
9 is odd, so the XOR of all 1 bits is 1
6 5 2 1
1 0 0 1 1 1 0 1 1 0 1 0 0 1 0 1 0 1 0 0 0
Final value
0b0000 0000 0011 1101 0001 0010 0101 0110 = 0x003D1256

## Slide 9: ECC Calculation - Syndrome
Syndrome = 46
Convert to binary
0b101110
Find a column that matches (Poll)
If so – bit in error (d9)
dX or pX
If 0 – no error
If no match – multiple errors
6 5 2 1
0 1 1 0 1 0 1 0 0 1 0 0 1 0 0 0

## Slide 10: Phase 9
Key observation – there are no new schematics, only Codasip updates
You will complete a real Verification exercise – writing a test to check your own hardware
This is a more realistic Verification exercise than Phase 3
Make sure your test covers an adequate number of cases of each error type

## Slide 11: Writeback Cache
On write hit, just update the block in cache
  Keep track of whether each block is dirty with a new bit
On a miss (read or write), a “Dirty” block must be replaced because we need that indexed block
  Write the dirty block back to memory
  Can use a write buffer to allow replacing block to be read first
  Read the addressed block from Main Memory
  On a write, write the new data to the cache line, set Dirty bit
Write back: a scheme in which reduces the number of potential stalls induced by the write buffer being full by updating values only to the block in cache, then writing the modified block to the lower level of the hierarchy when the block in cache is replaced
Dirty bit: an additional field in the cache memory that corresponds to whether the cache block has been written to

## Slide 12: Writeback Cache Write Buffer
Example of replacing a “dirty” cache block in a writeback cache using a write buffer
  Store the values of the “dirty” block in the write buffer
  Read and place the entries of the new block in cache from the next lower level of memory
  Restart the CPU (release stall)
  Write the data from the write buffer into memory as the CPU continues to execute on a write
A write buffer is an example of the great idea of parallelism. Data is being written to memory as CPU continues to execute.

## Slide 13: Write Allocation
What should happen on a write miss?
Alternatives for writethrough
  Allocate on miss: fetch the block (called write allocation)
  Write around to memory only: don’t fetch the block (called no write allocation)
    Keep Tag the same (different from the access)
    Since programs often write a whole block before reading it (e.g., initialization) – Spatial Locality – saves additional memory accesses
For writeback
  Usually fetch the block

## Slide 14: Cache Type Tradeoffs
WRITETHROUGH Cache
  Write Main Memory on every write
  Multiple writes to the same block cause multiple Main Memory writes
  No write allocation improves this somewhat
WRITEBACK Cache
  Fewer Main Memory writes overall
  Read misses cause Main Memory read + write
  Uses Spatial Locality to improve performance
  Somewhat more complex

## Slide 15: Cache Block Size Considerations
Larger blocks should reduce miss rate
  Due to spatial locality
  Examples, moving multiple instructions into a cache on a single cache miss due to the usual linear progression of code or multiple data array elements
But in a fixed-sized cache
  Larger blocks  fewer of them
    More competition  increased miss rate
Larger miss penalty
  More words required from lower in the memory hierarchy to fill the cache block
    Example: 1 word block = 8 cycle penalty while 4 word block miss penalty is 14 cycles (if Memory is 1 word wide)
  Can override benefit of reduced miss rate
  Early restart and critical word first can help
Early restart: resume execution as soon as the requested word of the block is available in the cache
Effectively hiding some of the cache miss penalty by overlapping the completion of the cache fill with the execution of the CPU – an example of parallelism
More commonly used in instruction caches due to the nature of code executing linearly while data not necessarily

## Slide 16: Optimizations
Assume 8 words per block
Memory is 1 word wide
Access time 8-2-2-2-2-2-2-2
Access address is word 3
Normal access sequence
  Remove stall after 22 cycles
Early restart sequence
  Remove stall after 14 cycles
Critical word first sequence
  Remove stall after 8 cycles
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7
0
1
2
3
4
5
6
7