## Slide 1: ECEN 3593-001 Computer Organization
Lecture #35
12 April 2021

## Slide 2: Agenda
Class Announcements
Course Project discussion
Chapter 5

## Slide 3: Class Announcements
Reading assignment for the week
  “Computer Organization and Design, The Hardware / Software Interface, RISC-V edition,” by David Patterson and John Hennessy
    ISBN 978-0-12-812275-4
    Chapter 5, “Large and Fast: Exploiting Memory Hierarchy”
    pages 410-449 (sections 5.5 thru 5.8)
OH today 2:00 to 3:00 in Zoom - https://cuboulder.zoom.us/j/4317981384

## Slide 4: Class Announcements
Phases 7/8 are in the deduction period – 1%/day
Phase 9 is in the deduction period – 4%/day
Phase 10 is posted
Target Date Sunday, April 18 at 10:00 PM
Bonus 1%/day, Deduction 4%/day
Homework #5 will be posted this week and due the following week

## Slide 5: Final Exam
May 3, 1:30 to 4:00 PM, Online
~20 Homework style questions
~30 short questions
Twice as many questions as the MidTerm, but 3 times as much time
The Final Exam is typically quite challenging
There will be a Practice Final available the week before the real Final

## Slide 6: Phase 9
To test:
  Create an input value
  Encode it
  Insert an error
  Decode the result
  Check that the result matches the Specification in Section 1
  Repeat
Make sure you try several data patterns
Make sure you exercise all the error cases

## Slide 7: Phase 10
Exercise of another key Computer Architecture function – optimization
Benchmark – a test program designed to exercise the functions required by a particular processor application
You each have a unique Benchmark – standardname10_test in H:
There is a full Codasip cache design in G:/Information/Phase 10
Your task is to determine the cache configuration which minimizes the cost function defined in your Benchmark
You create different cache configurations, build them and then run the Benchmark on that design

## Slide 8: Phase 10
Each configuration will take several minutes to build, and 2-3 minutes to run the Benchmark
Track the results of each run, and adjust the configuration based on your results
A minimum of 10 different configurations is required to be run
A report is required as part of the exercise, which has the opportunity for up to 75 bonus points
A report template is provided
The report is very representative of the type we use all the time in industry.

## Slide 9: Phase 10
Your regular score is a function of how close your final design is to the optimal one
This version of Phase 10 is new, so there may be typos or confusing language in the document
Please ask questions about the document in #phase10

## Slide 10: Phases 9 and 10
Questions??

## Slide 11: Direct Mapped Cache
Location determined by address
Direct mapped: only one index choice
  (Block address) modulo (#Blocks in cache)
#Blocks is a power of 2
Use Index address bits
Direct-mapped cache: a cache structure which each memory location is mapped to exactly one location in the cache
Block address/Index: The address used to address a block of memory in a cache or a level of memory hierarchy
How many bits would the Index include if there are 512 bytes in the cache with a block size of 4 words?
- 9 bits to address 512 bytes
- 7 bits to address 128 words
- 5 bits to address 32 blocks

## Slide 12: Tags and Valid bits
How do we know which particular block is stored in a cache location?
  Store block address as well as the data
  Actually, only need the high-order bits
  Called the tag
What if there is no data in a location?
  Valid bit: 1 = present, 0 = not present
  Initially 0
Tag: a field in a table used for a memory hierarchy that contains the address information required to identify whether the associated block in the hierarchy corresponds to a requested word
Example: In our 32-bit address RISC-V machine with a 512 byte cache, the address information to identify with a cache block would be 32-bits minus the 9-bits used to access the cache equating to upper 23-bits of the address
Valid bit: a field in the tables of a memory hierarchy that indicates that the associated block in the hierarchy contains valid data

## Slide 13: Cache Access Example
Memory – 32 lines, 1 word/line => 7 address bits (address shown)
Direct Mapped Cache – 8 lines
Initially all Valid bits are 0
1 word per line
Byte offset – address bits 1:0
No block offset
Index – address bits 4:2
Upper address – bits 6:5
0000000
0000100
0001000
0001100
0010000
0010100
0011000
0011100
0100000
0100100
0101000
0101100
0110000
0110100
0111000
0111100
1000000
1000100
1001000
1001100
1010000
1010100
1011000
1011100
1100000
1100100
1101000
1101100
1110000
1110100
1111000
1111100
Tag
Valid
Data
00
0
0000000
00
0
0000000
00
0
0000000
00
0
0000000
00
0
0000000
00
0
0000000
00
0
0000000
00
0
0000000
Index
000
001
010
011
100
101
110
111

## Slide 14: Cache Access Example
Read address 0100100
Index = 001 (0100100)
Valid = 0 => MISS
Copy data
Upper address = 01 (0100100)
Load to tag
Set Valid bit
Data to Processor
0000000
0000100
0001000
0001100
0010000
0010100
0011000
0011100
0100000
0100100
0101000
0101100
0110000
0110100
0111000
0111100
1000000
1000100
1001000
1001100
1010000
1010100
1011000
1011100
1100000
1100100
1101000
1101100
1110000
1110100
1111000
1111100
Tag
Valid
Data
00
0
0000000
00
0
0000000
00
0
0000000
00
0
0000000
00
0
0000000
00
0
0000000
00
0
0000000
00
0
0000000
Index
000
001
010
011
100
101
110
111
0100100
01
1

## Slide 15: Cache Access Example
Read address 1110100
Index = 101 (1110100)
Valid = 0 => MISS
Copy data
Upper address = 11 (1110100)
Load to tag
Set Valid bit
Data to Processor
0000000
0000100
0001000
0001100
0010000
0010100
0011000
0011100
0100000
0100100
0101000
0101100
0110000
0110100
0111000
0111100
1000000
1000100
1001000
1001100
1010000
1010100
1011000
1011100
1100000
1100100
1101000
1101100
1110000
1110100
1111000
1111100
Tag
Valid
Data
00
0
0000000
01
1
0100100
00
0
0000000
00
0
0000000
00
0
0000000
00
0
0000000
00
0
0000000
00
0
0000000
Index
000
001
010
011
100
101
110
111
1110100
11
1

## Slide 16: Cache Access Example
Read address 0100100
Index = 001 (0100100)
Valid = 1
Upper address = 01 (0100100)
Matches tag => HIT
Data to Processor
0000000
0000100
0001000
0001100
0010000
0010100
0011000
0011100
0100000
0100100
0101000
0101100
0110000
0110100
0111000
0111100
1000000
1000100
1001000
1001100
1010000
1010100
1011000
1011100
1100000
1100100
1101000
1101100
1110000
1110100
1111000
1111100
Tag
Valid
Data
00
0
0000000
01
1
0100100
00
0
0000000
00
0
0000000
00
0
0000000
11
1
1110100
00
0
0000000
00
0
0000000
Index
000
001
010
011
100
101
110
111
01
1
0010100

## Slide 17: Cache Access Example
Read address 1010100
Index = 101 (1010100)
Valid = 1
Upper address = 10 (1000100)
Does not match tag => MISS
Copy data
Update Tag
Data to Processor
0000000
0000100
0001000
0001100
0010000
0010100
0011000
0011100
0100000
0100100
0101000
0101100
0110000
0110100
0111000
0111100
1000000
1000100
1001000
1001100
1010000
1010100
1011000
1011100
1100000
1100100
1101000
1101100
1110000
1110100
1111000
1111100
Tag
Valid
Data
00
0
0000000
01
1
0100100
00
0
0000000
00
0
0000000
00
0
0000000
11
1
1110100
00
0
0000000
00
0
0000000
Index
000
001
010
011
100
101
110
111
1
11
1010100
10

## Slide 18: Cache Access Example
Read address 0001100
Valid = 0 MISS
Read address 1010100
Valid = 1, Match => HIT
Read address 1100100
Valid = 1, No match => MISS
0000000
0000100
0001000
0001100
0010000
0010100
0011000
0011100
0100000
0100100
0101000
0101100
0110000
0110100
0111000
0111100
1000000
1000100
1001000
1001100
1010000
1010100
1011000
1011100
1100000
1100100
1101000
1101100
1110000
1110100
1111000
1111100
Tag
Valid
Data
00
0
0000000
01
1
0100100
00
0
0000000
00
0
0000000
00
0
0000000
10
1
1010100
00
0
0000000
00
0
0000000
Index
000
001
010
011
100
101
110
111
1
00
0001100
0001100
1
1010100
1100100
11

## Slide 19: Direct Mapped Cache
Main Memory
…
Cache
Word A
Off
Ind
Upper
Address
Block/Line
B
Select Block
Tag
Select Block/Tag
Tag
Tag
Tag
Tag
Tag
Tag
Tag
Cmpr
Hit
MUX
Read Data
Block/Line
Word A
MUX
V
V
V
V
V
V
V
V
What is a problem with a Direct Mapped Cache?
Assume cache holds 16 words
LOOP: lw x5, 0x0(x2)
…
sw x6, 0x40(x2)
lw x7, 0x0(x2)
…
sw x8, 0x80(x2)
END: bne x15, x12, LOOP
Always miss on load

## Slide 20: N-way Set Associative Cache
Main Memory
Replicate the data and tag memory N times (N = 2^x) – N WAYs
Combine all Hit signals
If a hit, select the read data from the Way where the hit occurred
If a miss, read memory and replace the block (Tag and Data) in 1 Way
…
Cache
Word A
Off
Ind
Upper
Address
Block/Line
B
Select Block
Tag
Select Block/Tag
Cmpr
Tag
Tag
Tag
Tag
Tag
Tag
Tag
Cmpr
Cmpr
Cmpr
Cmpr
Cmpr
Cmpr
Cmpr
OR
Hit
MUX
Read Data
Block/Line
Word A
V
V
V
V
V
V
V
V
x N
Hit 0
Hit 1
Hit 2
Hit N
Hit
Way Select
Way 0

## Slide 21: N-way Set Associative Cache
Each location in Main Memory can map to MULTIPLE cache locations – one in each Way
The group of lines (one in each Way) which have the same Index are called a SET
Eliminates part of the aliasing problem (e.g. the loop)
Control logic is somewhat more complex

## Slide 22: Associative Caches
Fully associative
  Allow a given block to go in any cache entry
  Requires all entries to be searched at once
  Comparator per entry (expensive)
n-way set associative
  Each set contains n entries (ways)
  Block number (Index) determines which set
    (Block number) modulo (#Sets in cache)
  Search all entries in a given set at once
  n comparators (less expensive)
Fully associative cache: A cache structure in which a block an be placed in any location in the cache.
Set-associative cache: A cache that has a fixed number of locations (at least two) where each block can be placed.

## Slide 23: Associative Cache Example

## Slide 24: Spectrum of Associativity
For a cache with 8 total entries
1-Way Set Associative
2-Way Set Associative
4-Way Set Associative
8-Way Set Associative (fully associative)