## Slide 1: ECEN 3593-001 Computer Organization
Lecture #36
15 April 2021

## Slide 2: Agenda
Class Announcements
Course Project discussion
Chapter 5

## Slide 3: Class Announcements
Reading assignment for the week
  “Computer Organization and Design, The Hardware / Software Interface, RISC-V edition,” by David Patterson and John Hennessy
    ISBN 978-0-12-812275-4
    Chapter 5, “Large and Fast: Exploiting Memory Hierarchy”
    pages 410-449 (sections 5.5 thru 5.8)
OH today 2:00 to 3:00 in Zoom - https://cuboulder.zoom.us/j/4317981384

## Slide 4: Class Announcements
Phases 7/8 are in the deduction period – 1%/day
Phase 9 is in the deduction period – 4%/day
Phase 10 is posted
Target Date Sunday, April 18 at 10:00 PM
Bonus 1%/day, Deduction 4%/day
Homework #5 will be posted by tomorrow night
Due Thursday, April 22 at 10:00 PM
Today and Friday will be about the HW #5 problems

## Slide 5: Final Exam
May 3, 1:30 to 4:00 PM, Online
~20 Homework style questions
~30 short questions
Twice as many questions as the MidTerm, but 3 times as much time
The Final Exam is typically quite challenging
There will be a Practice Final available the week before the real Final

## Slide 6: Phase 9 Tips
Use multiple input data patterns for no error case
Make sure to exercise all possible single bit errors
Multiple starting patterns will help here also
Read the document carefully about requirements for the test
Make sure phase8_test passes

## Slide 7: Associativity Comparison – Direct Mapped
Assume a cache with 4 blocks, 1 word per block
Direct mapped
Access sequence (memory word address)
  0 – Miss (Valid = 0)
  8 – Miss (Replace)
  0 – Miss (Replace)
  6 – Miss (Valid = 0)
  8 – Miss (Replace)
  4 – Miss (Replace)
  8 – Miss (Replace)
  8 – Hit
  4 – Miss (Replace)
0
1
2
3
Index
Mem[0]
Mem[6]
Mem[8]
Mem[0]
Mem[8]
Hit Ratio = 1/9 = 11%
Mem[4]
Mem[4]
Mem[8]

## Slide 8: Associativity Comparison – 2-way Set Assoc.
Assume a cache with 4 blocks, 1 word per block
2-way Set Associative
Access sequence (memory word address)
  0 – Miss (Valid = 0)
  8 – Miss (Valid = 0)
  0 – Hit
  6 – Miss (Replace)
  8 – Miss (Replace)
  4 – Miss (Replace)
  8 – Hit
  8 – Hit
  4 – Hit
0
1
0
1
Way
Mem[0]
Mem[6]
Mem[8]
Mem[8]
Hit Ratio = 4/9 = 44%
Mem[4]
Set 0
Set 1

## Slide 9: Associativity Comparison – 4-way Set Assoc.
Assume a cache with 4 blocks, 1 word per block
4-way Set Associative
Access sequence (memory word address)
  0 – Miss (Valid = 0)
  8 – Miss (Valid = 0)
  0 – Hit
  6 – Miss (Valid = 0)
  8 – Hit
  4 – Miss (Valid = 0)
  8 – Hit
  8 – Hit
  4 – Hit
0
1
2
3
Way
Mem[0]
Mem[6]
Mem[8]
Hit Ratio = 5/9 = 55%
Mem[4]
Set 0

## Slide 10: Set Associative Cache Organization
Each Way must have its own comparator.
Each Way requires a multiplexor input
How many comparators would a 4,096 byte fully associative cache with a line of 4 words require?
  4,096 bytes / 4 bytes/word= 1,024 words
  1,024 words / 4 words/block = 256 blocks
  256 comparators and a 256:1 multiplexor!
The additional hardware for a fully associative cache makes it very expensive in terms of silicon real estate as well as execution time!
The increase in cache hit rate decreases with each additional level of associativity. Many systems find the cost / benefit trade off is in the range of 2 to 4.

## Slide 11: How Much Associativity
Increased associativity decreases miss rate
  But with diminishing returns
Simulation of a system with 64KB D-cache, 16-word blocks, SPEC2000
Miss ratio for various associativities
  1-way: 10.3% (this is a Direct Mapped cache)
  2-way: 8.6%
  4-way: 8.3%
  8-way: 8.1%

## Slide 12: Defining Cache Size
The size of a cache is the total number of bytes in all the Data Caches (not including the Tag memory)
An n-way Set Associative Cache of size X has X/n bytes per Way
The size of the Way defines how the Address is partitioned
The number of Ways does not affect the address partitioning since all Ways get the same address

## Slide 13: Defining Cache Size
Example – 8192 byte 4-way Set Associative Cache, 2 words per line, 32-bit words
  Bytes/Way = 8192/4 = 2048 bytes
  Words/Way = 2048/4 = 512 words
  Lines/Way = 512/2 = 256 lines
Byte Offset = 2 bits
Word Offset = 1 bit
Index = log2(256) = 8 bits
Tag = 32 – 8 – 2 – 1 = 21 bits

## Slide 14: Replacement Policy
Direct mapped: no choice
Set associative
  Select non-valid entry, if there is one
  Otherwise, choose among entries in the set
Least-recently used (LRU)
  Choose the one unused for the longest time
    Simple for 2-way, manageable for 4-way, too hard beyond that
Random
  Gives approximately the same performance as LRU for high associativity
Least recently used: a replacement scheme in which the block replaced is the one that has been unused for the longest time.

## Slide 15: Cache Behavior
Cache – 16 blocks of 1 word each
Address sequence (Word addresses)
What are the Upper Address bits (tags - aligned with the byte address) for a Direct Mapped Cache?
First – partition the address
2-way Set Associative cache of the same size – how many sets? (Poll)
14
402
27
123
59
30
567
18
Word
56
1608
108
492
236
120
2268
72
Byte
0x00000038
0x00000648
0x0000006c
0x000001ec
0x000000ec
0x00000078
0x000008dc
0x00000048
Hex
0…000000111000
0…011001000100
0…000001101100
0…000111101100
0…000011101100
0…000001111000
0…100011011100
0…000001001000
Binary
Offset
Index
0…000000000000
0…011001000000
0…000001000000
0…000011000000
0…000011000000
0…000001000000
0…100011000000
0…000001000000
Keep the Tag
Not in Tag
dec2hex()

## Slide 16: Cache Behavior
Cache – 16 blocks of 1 word each
What are the tags (aligned with the byte address) for a Direct Mapped Cache?
2-way Set Associative cache of the same size – how many sets?
What are the tags (aligned with the byte address) for this 2-way SA cache?
Cache contents after the address sequence with LRU starting from power up
This access is a hit
14
402
27
123
59
30
567
27
Word
56
1608
108
492
236
120
2268
108
Byte
0x00000038
0x00000648
0x0000006c
0x000001ec
0x000000ec
0x00000078
0x000008dc
0x0000006c
Hex
0…000000111000
0…011001000100
0…000001101100
0…000011101100
0…000011101100
0…000001111000
0…100011011100
0…000001101100
Binary
Offset
Index
0…000000100000
0…011001000000
0…000001100000
0…000011100000
0…000011100000
0…000001100000
0…100011000000
0…000011000000
Keep the Tag
Not in Tag
010b
011b
000b
001b
110b
111b
100b
101b
Index
27
402
14
567
W0
123
W1
8 Sets

## Slide 17: Cache Behavior
Cache – 16 blocks of 1 word each
What are the tags (aligned with the byte address) for a Direct Mapped Cache?
2-way Set Associative cache – how many sets?
What are the tags (aligned with the byte address) for this 2-way SA cache?
Cache contents after the address sequence with LRU starting from power up
This is a Replacement due to the Miss
Why did we replace in Set 1?
LRU – Set 0 was accessed more recently
14
402
27
123
59
30
567
27
Word
56
1608
108
492
236
120
2268
108
Byte
0x00000038
0x00000648
0x0000006c
0x000001ec
0x000000ec
0x00000078
0x000008dc
0x00000048
Hex
0…000000111000
0…011001000100
0…000001101100
0…000011101100
0…000011101100
0…000001111000
0…100011011100
0…000001001000
Binary
Offset
Index
0…000000100000
0…011001000000
0…000001100000
0…000011100000
0…000011100000
0…000001100000
0…100011000000
0…000001000000
Keep the Tag
Not in Tag
010b
011b
000b
001b
110b
111b
100b
101b
Index
18
59
402
14
567
Set 0
30
Set 1
8 Sets
27

## Slide 18: Cache Behavior
Cache – 16 blocks of 1 word each
What are the tags (aligned with the byte address) for a Direct Mapped Cache?
2-way Set Associative cache – how many sets?
What are the tags (aligned with the byte address) for this 2-way SA cache?
Cache contents after the address sequence with LRU starting from power up
How many blocks were replaced?
  1
What is the hit ratio for this sequence?
  1/8 = 12.5%
14
402
27
123
59
30
567
18
Word
56
1608
108
492
236
120
2268
72
Byte
0x00000038
0x00000648
0x0000006c
0x000001ec
0x000000ec
0x00000078
0x000008dc
0x00000048
Hex
0…000000111000
0…011001000100
0…000001101100
0…000011101100
0…000011101100
0…000001111000
0…100011011100
0…000001001000
Binary
Offset
Index
0…000000100000
0…011001000000
0…000001100000
0…000011100000
0…000011100000
0…000001100000
0…100011000000
0…000001000000
Keep the Tag
Not in Tag
010b
011b
000b
001b
110b
111b
100b
101b
Index
18
59
402
14
567
Set 0
27
30
Set 1
8 Sets