## Slide 1: ECEN 3593-001 Computer Organization
Lecture #4
25 January 2021

## Slide 2: Agenda
Class Announcements
RISC-V Assembly Language

## Slide 3: Class Announcements
Reading for the week
  “Computer Organization and Design, The Hardware / Software Interface, RISC-V edition,” by David Patterson and John Hennessy
    ISBN 978-0-12-812275-4
    Chapter 2, “Language of the Computer”
      sections 2.1 thru 2.8
      pages 60-108 (sections 2.1 thru 2.8)
RISC-V Specification is in the Course Content Area
Everyone has joined Slack and signed the NDA!!!

## Slide 4: Class Announcements
Phase 1 Target Date Thursday, January 28 at 10:00 PM
Phase 2 will be posted before class on Wednesday
Phase 2 Target Date Sunday, February 7 at 10:00 PM
Bonus – 1% per day (maximum 7%), Deduction 10%/day
Assignment due dates and Phase Target Dates will be specified in class – the Syllabus is just a rough estimate
Late excuses – I must know BEFORE the assignment is due
Follow Slack, use notifications if necessary

## Slide 5: Class Announcements
Homework #1 will be posted by the end of Wednesday
Due Thursday, February 4 at 10:00 PM
Random selection of questions on the RISC-V ISA

## Slide 6: Class Project Phase 1
If you have successfully submitted Phase 1, you should be able to see your grade in Canvas
Let me know in Slack if you cannot see your score

## Slide 7: Instructions: Language of the Computer (Chapter 2)
Instruction Set Architecture = Computer Architecture
Different computers have different instruction sets
  But with many aspects in common
Early computers had very simple instruction sets
  Simplified implementation
  MISC (Minimal Instruction Set Computers): Stack base
    No addressing of operands
Many modern computers also have simple instruction sets
  RISC (Reduced Instruction Set Computers)

## Slide 8: The RISC-V Instruction Set Architecture (ISA)
Used as the example throughout the book
Developed at UC Berkeley as an open ISA
Now managed by the RISC-V Foundation (riscv.org)
Typical of many modern ISAs
  The RISC-V green sheet is a good example of these modern ISAs
Similar ISAs have a large share of embedded core market
  Applications in consumer electronics, network/storage equipment, cameras, printers, …

## Slide 9: The RISC-V Instruction Set Architecture (ISA)
The instruction set is a key component in defining the architecture (hence ISA)
A complete understanding of the instruction set behavior is critical in developing the hardware
What drives the ISA
  Hardware design considerations (frequency, area and power)
  Software performance considerations (primarily higher level language Compilers like C)
  Tradeoffs between these

## Slide 10: The RISC-V Instruction Set Architecture (ISA)
We will explore the ISA at three levels
  Assembly Language
  Machine Language
  Basic (single cycle) hardware
The textbook isn’t organized exactly like this
The lectures will include information not in the book, which will be on homework and exams

## Slide 11: The RISC-V Instruction Set Architecture (ISA)
RISC ISAs are built around a set of Registers which hold data
The set is referred to as the Register File
In RISC-V there are 32 registers
Can be 32-bit, 64-bit or 128-bit in RISC-V
We will focus on a 32-bit wide Register File, although the book example is a 64-bit architecture
This ISA is called R32VI (32 bits, I for integer)
Code written with the ISA instructions is Assembly Language

## Slide 12: RISC-V: The constant zero
RISC-V register 0 (x0) is the constant 0
  Cannot be overwritten
  The hardware implementation prevents x0 from being overwritten
Useful for common operations
  E.g., move between registers
  add x5, x20, x0
  x5 = x20 + 0
  Value in x20 is moved to x5
Enables a smaller instruction set!
  Simplicity is the art of design

## Slide 13: Unsigned Binary Integer
Data contains 32 bits, numbered from 31 (MSb) to 0 (LSb)
Given an n-bit number
Range: 0 to +2^n – 1
Example
  0000 0000 0000 0000 0000 0000 0000 1011 = 0 + … + 1×2^3 + 0×2^2 +1×2^1 +1×2^0 = 0 + … + 8 + 0 + 2 + 1 = 11
Using 32 bits: 0 to +4,294,967,295
Using 64 bits: 0 to +18,446,774,073,709,551,615
In C, “unsigned int”
variable declaration

## Slide 14: 2s-Complement Signed Integers
Given an n-bit number
Range: –2^(n – 1) to +2^(n – 1) – 1
Example
  1111 1111 1111 1111 1111 1111 1111 1100 = –1×2^31 + 1×2^30 + … + 1×2^2 +0×2*1 +0×2^0 = –2,147,483,648 + 2,147,483,644 = –4
Using 32 bits: –2,147,483,648 to +2,147,483,647
Using 64 bits: -9,223,372,036,854,775,808 to 9,223,372,036,854,775,807
In C, “int”
variable declaration

## Slide 15: 2s-Complement Signed Integers
Bit 31 is sign bit in 32 bits and Bit 63 is sign bit in 64 bits
  1 for negative numbers
  0 for non-negative numbers
2n – 1 can’t be represented
Non-negative numbers have the same unsigned and 2s-complement representation
Some specific numbers
  0: 0000 0000 … 0000
  –1: 1111 1111 … 1111
  Most-negative: 1000 0000 … 0000 –2,147,483,648 / -9,223,372,036,854,775,808
  Most-positive: 0111 1111 … 1111 +2,147,483,647 / 9,223,372,036,854,775,807

## Slide 16: 2s-Complement Signed Integers
Complement and add 1
  Complement means 1 → 0, 0 → 1
Example: negate +2
  +2 = 0000 0000 … 0010
  –2 = 1111 1111 … 1101 + 1 = 1111 1111 … 1110

## Slide 17: Why 2’s Complement?
A = B + C is correct independent of the sign of A, B or C
Other representations (1’s complement, sign/magnitude, etc.) don’t have this characteristic
Adder doesn’t need to handle the sign bit differently
sub a,b = add a, (2’s complement of b)

## Slide 18: Overflow
Overflow occurs if right most bits that describe a number cannot be represented by the right most hardware bits
  For example:
    If representing a number requires more than 31-bits in a 32-bit word, the right most bits in the hardware cannot describe the number
    Similarly, if the 15-bits in a 16-bit value, the right most bits in the hardware cannot describe the number
  Overflows occurs when the left most retained bit of the binary bit pattern is not the same as the infinite number of digits to the left (the sign bit is incorrect)
    Example (8-bits): add 0b01111111 to 0b01111111 (largest positive number)
    Result is 0b11111110 – sign is 1 but infinite left digits are 0

## Slide 19: Fun with Numbers
Binary
Decimal
Hex(adecimal)
Power of 2
Power of 10
Power of 16
0b1011
245
0x3a6b
b(inary dig)it = bit
digit
nibble
Common processor unit is a byte = 8 bits (two nibbles)
Convenient for characters (e.g. ASCII)
0xA4 is one byte
0x1ab7 = 1 x 16^3 + 10 x 16^2 + 11 x 16^1 + 7 x 16^0
= 4096 + 2560 + 176 + 7 = 6839

## Slide 20: Critically Important Functions
1024 = kilo (kibi in textbook) = K
1048576 = mega (mebi) = M
1073741824 = giga (gibi) = G
Lower case = power of 10

## Slide 21: RISC-V: Basic RV32I Instruction Set
Seven basic instruction groups
  Register (3 address) – add/sub/and/or/xor/slt/sltu/sll/srl/sra
  Immediate – addi/andi/ori/xori/slti/sltui/slli/srli/srai
  Memory Load – lw/lh/lhu/lb/lbu
  Memory Store – sw/sh/sb
  Conditional Branch – beq/bne/blt/bltu/bge/bgeu
  Jump – jal/jalr
  Upper immediate – lui/auipc

## Slide 22: RISC-V: Register (3 address) Instructions
Operate on three register operands
  One destination and two sources
add x1, x2, x3 // x1 gets x2 + x3
The destination register is always first
All arithmetic/logical/shift operations have this form
Add/sub – signed arithmetic as expected

## Slide 23: RISC-V: Logical Instructions
Bitwise Operations on three register operands
  Two sources and one destination
and x1, x2, x3 // x1 gets x2 AND x3
or x1, x2, x3 // x1 gets x2 OR x3
xor x1, x2, x3 // x1 gets x2 XOR x3

## Slide 24: RISC-V: AND Operations
Useful to mask bits in a word
  Select some bits, clear others to 0
and x12, x10, x11
x10 = 0b0110 0001 1100 1110 0111 0010 1010 1001
x11 = 0b1111 1111 0000 0000 0000 0000 1111 1111
x12 = 0b0110 0001 0000 0000 0000 0000 1010 1001

## Slide 25: RISC-V: OR Operations
Useful to include bits in a word
  Set some bits to 1, leave others unchanged
or x12, x10, x11
x10 = 0b0110 0001 1100 1110 0111 0010 1010 1001
x11 = 0b1111 1111 0000 0000 0000 0000 1111 1111
x12 = 0b1111 1111 1100 1110 0111 0010 1111 1111

## Slide 26: RISC-V: Mask/Merge with AND/OR
Want lower half of x10 and upper half of x11 in x12
x10 = 0b0110 0001 1100 1110 0111 0010 1010 1001
x11 = 0b1101 1001 1110 0010 1101 0101 1100 1100
x13 = 0b0000 0000 0000 0000 1111 1111 1111 1111
x14 = 0b1111 1111 1111 1111 0000 0000 0000 0000
and x10, x10, x13
x10 = 0b0000 0000 0000 0010 0111 0010 1010 1001
and x11, x11, x14
x11 = 0b1101 1001 1110 0010 0000 0000 0000 0000
or x12, x10, x11
x12 = 0b1101 1001 1110 0010 0111 0010 1010 1001