## Slide 1: ECEN-CSCI 3593-001 Computer Organization
Lecture #5
27 January 2021

## Slide 2: Agenda
Class Announcements
RISC-V Assembly Language

## Slide 3: Class Announcements
Reading for the week
  “Computer Organization and Design, The Hardware / Software Interface, RISC-V edition,” by David Patterson and John Hennessy
    ISBN 978-0-12-812275-4
    Chapter 2, “Language of the Computer”
      sections 2.1 thru 2.8
      pages 60-108 (sections 2.1 thru 2.8)
RISC-V Specification is in the Course Content Area

## Slide 4: Class Announcements
Phase 1 Target Date tomorrow at 10:00 PM
  19 people have not submitted – DO NOT GET BEHIND!
Phase 2 is posted
  Target Date Sunday, February 7 at 10:00 PM
  Bonus 1%/day (maximum 7%), Deduction 10%/day
  Note additional documentation in the Debug section of Canvas
  Don’t be fooled by Phase 1 – everything now will be much more complex
Homework #1 is posted
  Due Thursday, February 4 at 10:00 PM
  NOTE: Randomized questions

## Slide 5: Homework #1
Material presented this week
Work carefully through the assignment – the instructions must be understood exactly
If you use a calculator for hex <-> binary <-> decimal conversion, be careful about the number of bits represented

## Slide 6: TA Office Hours
Please respond to the Doodle Poll posted in #general and below
https://doodle.com/poll/ha6ape64zugquqvs?utm_source=poll&utm_medium=link
Select times that work for you for TA Office Hours
We will select times and announce them before next Monday
You can still contact me any time

## Slide 7: Audio Interruptions
Talked to Zoom about why I can’t hear you – they have no clue
Tested this at home and it worked – maybe speak louder?
Please “Raise Hand” if you have a question, and unmute
I will pause at the end of each slide so you can interrupt

## Slide 8: RISC-V: XOR Operations
Differencing operation
  Invert some bits (1 -> 0, 0 -> 1), leave the others unchanged
Xor x12, x10, x11
x10 = 0b0110 0001 1100 1110 0111 0010 1010 1001
x11 = 0b1111 1111 0000 0000 0000 0000 1111 1111
x12 = 0b1001 1110 1100 1110 0111 0010 0101 1001

## Slide 9: RISC-V: Register (3 address) Instructions
SLT – “set less than”
slt x5, x6, x7
If x6 is less than x7 (as signed numbers):
  Set x5 to 1
  Else set x5 to 0
SLTU – compare x6 and x7 as unsigned numbers
Signed value 0xffffffff (-1) < 0x00000001 (1)
Unsigned value 0xffffffff (2^32-1) > 0x00000001 (1)

## Slide 10: RISC-V: Register (3 address) Instructions
Shift instructions
shift x10, x11, x12
Shift the value in x11 by the (unsigned) number of bits in x12 and store in x10
  sll – shift left logical – fill with 0’s on the right
  srl – shift right logical – fill with 0’s on the left
  sra – shift right arithmetic – fill with the sign on the left
Why no sla? (POLL)

## Slide 11: RISC-V: Register (3 address) Instructions
Shift example
shift x10, x11, x12
Assume x11 = 0b1010 1101 1001 0101 1100 1010 1100 1011
sll by 7 x10 = 0b1100 1010 1110 0101 0110 0101 1000 0000
srl by 9 x10 = 0b0000 0000 0101 0110 1100 1010 1110 0101
sra by 5 x10 = 0b1111 1101 0110 1100 1010 1110 0101 0110

## Slide 12: RISC-V: Immediate Instructions
Replace one register with a 12-bit signed immediate value
  One destination and two sources (one immediate) and
addi x2, x3, 0x15 // x2 gets x3 + 0x15
All arithmetic/logical/shift operations have this form
Addi – arithmetic as expected
Why no subi? (POLL)

## Slide 13: RISC-V: Immediate Instructions
The 12-bit immediate is SIGN EXTENDED to 32 bits
0x345 => 0x00000345
0xA67 => 0xFFFFFA67
-27 (12-bit immediate) => -27 (32 bit value)
0xFE6 = 0xFFFFFFE6
What is the 32 bit value of 0x927? (POLL)

## Slide 14: Sign Extension
Representing a number using more bits
  Preserve the numeric value
In RISC-V instruction set
  addi,slti: extend immediate value
  lb, lh,sw: extend loaded byte/halfword
  beq, bne,jal: extend the displacement (enabling branches forward and backwards)
The function of a signed operation is to copy the sign repeatedly to fill the rest of the register – called sign extension
  The non-signed bits to the right are copied to their original bit location in the new larger word
  Compared to unsigned values: extend with 0s
Examples: 8-bit to 16-bit
  +2: 0000 0010 => 0000 0000 0000 0010
  –2: 1111 1110 => 1111 1111 1111 1110

## Slide 15: RISC-V: Immediate Instructions
Equivalents of all Register instructions
  andi, ori, xori
  slti, sltiu
  slli, srli, srai (5/6 bit immediate, always positive)

## Slide 16: RISC-V: NOT Operation
Useful to invert bits in a word
  Change 0 to 1, and 1 to 0
RISC-V does not have a NOT operation
But, a RISC-V xori instruction can become a NOT Operation
xori x5, x6, 0xfff
=> not x5, x6
“not” is a Pseudo instruction
The 12-bit signed immediate 0xfff becomes a 32-bit word of all 1s
Example of keeping it simple
By not adding another instruction

## Slide 17: Data Memory
RISC-V has a Data Memory
Accessed by load and store instructions
Instruction generates a byte address
Byte at 0x000b
Halfword at 0x0002
Word at 0x0018

## Slide 18: RISC-V: Memory Load Instructions
Load a Register with the contents of a memory location
One destination and two sources (one immediate)
lw x7, 0x20(x8) // x7 gets the contents of the memory at address // (x8 + 0x20)
Similar to Immediate instructions (2 registers + 12-bit sign extended immediate)
The register (like x8) is referred to as the Base Address
The constant (like 0x20) is referred to as the Offset
Their sum is the memory address being accessed

## Slide 19: RISC-V: Memory Load Instructions
5 load instructions
  lw – load a 32-bit word
  lh – load a 16-bit sign extended halfword
  lhu – load a 16-bit zero extended (unsigned) halfword
  lb – load an 8-bit sign extended byte
  lbu – load an 8-bit zero extended (unsigned) byte
The full 32-bit register is always loaded
The loaded byte/halfword is in the lower register bits
Zero extended (lbu/lhu) or sign extended (lb/lh)

## Slide 20: RISC-V: Memory Store Instructions
Store the contents of a Register to a memory location
  Three sources (2 registers and one immediate) and NO destination
sw x7, 0x20(x8) // the memory at address (x8 + 0x20) gets // the value in x7
Similar to Immediate instructions (2 registers + 12-bit sign extended immediate)
Address calculated exactly like Loads

## Slide 21: RISC-V: Memory Store Instructions
3 store instructions
  sw – store a 32-bit word
  sh – store a 16-bit halfword
  sb – store an 8-bit byte
The stored byte/halfword comes from the lower register bits
Only the selected memory element (byte/halfword/word) at the specified address is modified

## Slide 22: RISC-V: Memory Operands Example
C code:
A[12] = h + A[8];
  h in x18, base address of A (an array of words) in x20
Compiled RISC-V code:
  Index 8 requires offset of 32 (8*4)
  Index 12 requires offset of 48 (12*4)
lw x5, 32(x20) # load word from A[8] add x5, x18, x5 sw x5, 48(x20) # store word to A[12]

## Slide 23: RISC-V: Allows byte addressability, but it is based on 32-bit instructions and data words!
Alignment Restrictions:
  To access a 32-bit word, the address should be a multiple of 4
  To access a 16-bit halfword, the address should be a multiple of 2
  RISC-V supports unaligned addresses but performance may be very poor. The class project will not implement this functionality.

## Slide 24: Why are unaligned addresses a Problem?
6
5
4
6
5
4
6
5
4
3
0
1
2
3
4
5
6
7
3
4
5
6
0
1
2
7
3
3
Read
Shift
Read
Shift
Merge
lw x7, x0(3)

## Slide 25: RISC-V: Memory Operands
Main memory used for composite data
  Arrays, structures, dynamic data
To apply arithmetic operations
  Load values from memory into registers
  Store result from register to memory
Memory is byte addressed
  Each address identifies an 8-bit byte
Words should be aligned in memory
  Address should be a multiple of 4
RISC-V is Little Endian
  Least-significant byte at least address of a word
  Compared to Big Endian: Most-significant byte at least address
Load/Store Machine
Must multiply word increments by 4 due words = 4 bytes

## Slide 26: Endianness
Execute sh x4, 0(x0)
Endianness is a description of the RELATIONSHIP between the processor and memory
x4 = 0x0A0B0C0D
Execute sw x4, 0(x0)
0
1
2
3
0D
0C
0B
0A
Little Endian
0
1
2
3
0A
0B
0C
0D
Big Endian
0D
0C
0C
0D

## Slide 27: Endianness
Could a Big Endian machine fetch the same byte of data at the same byte address as a little Endian machine? (POLL)
Big Endian architectures: MIPS, ARM, 68000, AVR32
Little Endian architectures: RISC-V, x86, Altera Nios