## Slide 1: ECEN 3593-001 Computer Organization
Lecture #6
29 January 2021

## Slide 2: Agenda
Class Announcements
Assembly Language/Machine Language (possibly)

## Slide 3: Class Announcements
Reading for the week
  “Computer Organization and Design, The Hardware / Software Interface, RISC-V edition,” by David Patterson and John Hennessy
    ISBN 978-0-12-812275-4
    Chapter 2, “Language of the Computer”
      sections 2.1 thru 2.8
      pages 60-108 (sections 2.1 thru 2.8)
The RISC-V Specification is in Content/Course Material/RISC-V Documentation/riscv-spec-v2.2.pdf.
  The chart on page 104 is essential
Homework 1 assigned – Due Thursday, February 4 at 10:00 pm

## Slide 4: Class Announcements
Phase 1 is in the deduction period – 25%/day
Phase 2 is posted.
The Target Date is Sunday, February 7 at 10:00 PM
Bonus 1%/day before that. Deduction 10%/day after that.

## Slide 5: TA Office Hours
23 respondents for Doodle Poll – thanks!
Will announce TA OH schedules by Monday

## Slide 6: Phase 2 Note
ia_utils.codal defines the functions in the RISC-V ALU.
We want to minimize the ALU logic and therefore minimize the number of functions.
Exactly 11 functions are required, and these are included in the commented sections of ia_utils. Designs with more than 11 choices will be rejected.
DO NOT modify any functions or add any new ones.

## Slide 7: Phase 2 – switch Syntax
In a C switch statement, 2 ways to implement cases
Multiple cases for a single function (as in Phase1_orig)
Separate function for each case
Can mix and match these

## Slide 8: Phase 2 Common Error #1
You have tried to build the program when a simulation was running

## Slide 9: Phase 2 Common Error #2
You have tried to build the hardware project when a simulation was running
Always terminate the simulation with the red button before you do anything else

## Slide 10: Registers vs Memory
Registers are faster to access than memory
  add x5, x6, x7
Operating on memory data requires loads and stores
  More instructions required to be executed
    lw x5, 0(x19)
    add x5, x5, x7
    sw x5, 0(x19)
Compiler must use registers for variables as much as possible
  Only “spill” to memory for less frequently used variables
  Register optimization is important!
  Example of “Make the Common Case Fast”

## Slide 11: RISC-V: Registers (convention)
x0: the constant value 0 (hardwired)
x1: return address
x2: stack pointer
x3: global pointer
x4: thread pointer
x5-x7, x28-x31: temporaries
x8: frame pointer
x9, x18-x27: saved registers
x10-x11: function arguments / results
x12-x17: function arguments

## Slide 12: Instruction Memory
RISC-V has an Instruction Memory
Accessed by the Program Counter (PC)
Byte addresses, but only word accesses
Can be at the same addresses as the Data Memory
In the Class Project, memories will be separate

## Slide 13: RISC-V: Conditional Branch Instructions
Instructions are fetched from the Instruction Memory at an address specified by the Program Counter (PC)
After a normal fetch, PC increments by 4 (byte address)
Branches and jumps load the PC with a different value

## Slide 14: RISC-V: Conditional Branch Instructions
Conditional branches load the PC based on a comparison of two registers
branch x7, x8, 0x10 // If x7 and x8 satisfy the branch condition, // PC = PC + 0x10
// else PC = PC + 4
Similar to Immediate instructions (2 registers + 12-bit signed immediate, the branch offset)

## Slide 15: RISC-V: Conditional Branch Instructions
6 Branch Instructions
  beq – branch if registers equal
  bne – branch if registers not equal
  blt – branch if register 1 < register 2 (as signed numbers)
  bltu – branch if register 1 < register 2 (as unsigned numbers)
  bge – branch if register 1 >= register 2 (as signed numbers)
  bgeu – branch if register 1 >= register 2 (as unsigned numbers)
Immediate (called the “branch offset”) is a signed value
In Assembly Language the target is usually a label, and the Assembler computes the branch offset from the label address

## Slide 16: Signed vs. Unsigned Conditional Branches
Signed comparison: blt, bge
Unsigned comparison: bltu, bgeu
Example
  x22 = 1111 1111 1111 1111 1111 1111 1111 1111
  x23 = 0000 0000 0000 0000 0000 0000 0000 0001
  x22 < x23 // signed
    –1 < +1
  x22 > x23 // unsigned
    +4,294,967,295 > +1

## Slide 17: RISC-V: Conditional Branch Instructions
There isn’t a bgt instruction – why? (POLL)
Can create it from other instructions
  bgt x2, x3, TARGET is the same as
  blt x3, x2, TARGET
There are several Pseudo Instructions like this to make writing Assembly Language easier

## Slide 18: RISC-V: Jump Instructions
Jumps are unconditional branches with special characteristics
jal x5, 0x12348 (Jump And Link) – J-type (UJ-type in book)
  Load register x5 with (Current PC + 4)
  Set PC to (Current PC + 0x12348)
jalr x5, 0x24(x6) (Jump And Link Register) – I-type
  Load register x5 with (Current PC + 4)
  Set PC to (Value in register x6 + 0x24)
  Similar to Immediate instructions (2 registers + 12-bit signed immediate)

## Slide 19: Procedure Call
Steps required
  Place parameters (arguments) in registers x10 to x17
  Transfer control to procedure
  Perform procedure’s operations
  Place result in register for caller
  Return to place of call + 1 instruction (address in x1)
Definition: Return Address is the address that a called procedure uses to return to the caller procedure.

## Slide 20: Procedure Call Instructions
Procedure call: jump and link
jal x22, ProcedureLabel
  Address of following instruction (PC + 4) is put in register x22
  Jumps to target address defined by ProcedureLable (20 bit address)
  Using x0 as destination creates a normal jump (x0 cannot be changed)
Procedure return: jump and link register
jalr x17, offset(x22)
  Address of following instruction (PC + 4) is put in register x17
  Jumps to target address which is offset + x22
  x0 is typically the register used as the destination in the JALR
  Can also be used for vectored branches
    e.g. for case/switch statements
  Can generate odd (i.e. illegal) instruction addresses

## Slide 21: JAL/JALR Example
Call the function at LABEL
  PC + 4 -> x3
Execute the function
Return to return address
Can save return address here too

## Slide 22: RISC-V: Jump Instructions
jalr also allows the implemented of a VECTORED BRANCH
Assume register x9 contains the base of a table (TABLE) in the Instruction Memory
Assume register x10 contains an offset into that table
add x7, x9, x10 // Get the specific pointer into x7
jalr x5, 0x0(x7) // Branch to selected routine
TABLE: // Routine 1
TABLE + 16: // Routine 2
TABLE + 32: // Routine 3

## Slide 23: RISC-V: Upper Immediate Instructions
Since the standard immediate is in the lower 12 bits, we need a way to create a 32-bit constant
20-bit Immediate in upper 20 bits, 0 in lower bits
lui x22, 0x12345 (Load Upper Immediate)
=> x22 = 0x12345000
No sign extension required

## Slide 24: RISC-V: 32-bit Constants
Most constants are small
  12-bit immediate is sufficient
For the occasional 32-bit constant (e.g. 0x003D0500)
lui rd, constant
  Copies 20-bit constant to bits [31:12] of rd
  Extends bit 31 to bits [63:32] if 64-bit CPU
  Clears bits [11:0] of rd to 0
0000 0000 0011 1101 0000
0000 0000 0000 0000
lui x19, 976 // 0x003D0
addi x19,x19,128 // 0x500
0000 0000 0000 0000
0000 0000 0000
0000 0000 0011 1101 0000
0000 0000 0000 0000
0000 0000 0000 0000
0101 0000 0000
Do you see a potential issue with this two instruction sequence? (P)
What happens with the 12th bit of the addi immediate? (P)

## Slide 25: RISC-V: 32-bit Constants
If the 12 bit is a negative sign bit, “1,” the following sequence will work and will be used in your Codasip Project
  It will work in all cases, “1” or “0” sign bit in the 12-bit imm.
Assuming 32-bit registers as in the course Codasip Project
  lui x19, 976 // 0x3d0
  addi x5, x0, 2548 // 0xd48
  slli x5, x5, 20 // push the 20 sign extended bits out of reg
  srli x5, x5, 20 // right justify 12 bit constant
  add x19, x19, x5 // combine for 32-bit constant (0x003d0d48)
How could we implement 1 new instruction to save 3?

## Slide 26: RISC-V: 32-bit Constants
Create an “unsigned immediate”, say addiu
Assuming 32-bit registers as in the course Codasip Project
  lui x19, 976 // 0x003d0(000)
  addiu x19, x19, 2548 // 0x(00000)d48 – NOT SIGN EXTENDED
  slli x5, x5, 20 // push the 20 sign extended bits out of reg
  srli x5, x5, 20 // right justify 12 bit constant
  sdd x19, x19, x5 // combine for 32-bit constant (0x003d0d48)