## Slide 1: ECEN 3593-001 Computer Organization
Lecture #7
1 February 2021

## Slide 2: Agenda
Class Announcements
RISC-V instruction Formats

## Slide 3: Class Announcements
Reading for the week
  “Computer Organization and Design, The Hardware / Software Interface, RISC-V edition,” by David Patterson and John Hennessy
    ISBN 978-0-12-812275-4
    Chapter 2, “Language of the Computer”
      sections 2.1 thru 2.8
      pages 60-108 (sections 2.1 thru 2.8)
RISC-V Specification is in the Course Content Area
Office Hours today 2:00 to 3:00 – Zoom

## Slide 4: Class Announcements
Homework #1 is due Thursday, February 4 at 10:00 PM
Phase 2 is posted.
The Target Date is Sunday, February 7 at 10:00 PM
Bonus 1%/day before that. Deduction 10%/day after that.

## Slide 5: TA Office Hours
New document in Canvas describing TA Office Hours
2 hours each day of the week except Saturday, based on Doodle Poll results
TAs will have open Zoom meetings you can connect to
Can Slack me any time, and request office hours with me any time
I will open a Zoom meeting from 2:00 to 3:00 today – fell free to join at https://cuboulder.zoom.us/j/4317981384. This will be an experiment.

## Slide 6: Phase 2 Structure
Main execution loop
Functions used elsewhere
Defines the machine code for instructions
Defines the instruction implementation

## Slide 7: Phase 2 Note – Pseudo Instructions
Defined for programming clarity
Instructions which are not part of the ISA, but map to ISA instructions
Examples
  mv, x2, x1 -> addi x2, x1, 0
  bnez x1, LABEL -> bne x1, x0, LABEL
Defined by i_instruction_alias group in isa.codal (e.g. i_mv_alias)
All created by uncommenting – removal of /* and */
Simplicity!!

## Slide 8: Latest Processor Forecast 2023
Big new areas
  Hearables (smart earbuds)
  Smart Speakers (Home devices)
  Smartwatches (all bands)
These were small in 2018

## Slide 9: RISC-V: 32-bit Constants
To create the 32-bit constant 0x003d0d48
  lui x5, 0x003d0
  addi x5, x0, 0xd48
BUT – SIGN EXTENSION causes this to fail – result is
  0x003c9d48

## Slide 10: RISC-V: 32-bit Constants
How could the compiler handle 32-bit constants?
Modify the lui immediate to compensate
In previous example – want 0x003D0D48
We’re going to add 0xFFFFFD48 to the upper immediate
This is like adding 0x00000D48
And then 0xFFFFF000, which is -0x1000
So add +0x1000 to the LUI value, which is +0x1 to the constant
lui x19, 0x003D1
addi x19, x19, 0xD48
Result – x19 = 0x003D0D48

## Slide 11: RISC-V: Upper Immediate Instructions
auipc x27, 0x00001 (Add Upper Immediate to PC)
=> x27 = Current PC + 0x00001000
Allows software to determine the program location in memory
Can access data embedded in the program
The only obvious mistake (to me) in the RISC-V ISA – we really want to add a normal immediate
ECEN 4593-001 lecture 9

## Slide 12: RISC-V: Machine Language
Assembly Language is a human readable description of the instructions to be executed
Machine Language is a machine readable description
Patterns of 1’s and 0’s held in the Instruction Memory
What Great Idea of Computer Architecture is apparent here?
Abstraction – Assembly Language is an Abstraction of Machine Language
In RV32I all instructions are 32 bits
Simplicity is the art of design!

## Slide 13: RISC-V Instruction Set Architecture (ISA)

## Slide 14: RISC-V Instruction Formats
From Page 104

## Slide 15: RISC-V R-type instructions
The layout of the instruction is called the instruction format
Each segment in the instruction is called a field
Instruction fields
  opcode: operation code (format e.g. R-type is a function of the opcode)
  rd: destination register number
  funct3 (or fn3): 3-bit function code (additional opcode)
  rs1: the first source register number
  rs2: the second source register number
  funct7 (or fn7): 7-bit function code (additional opcode)

## Slide 16: RISC-V R-type Instruction Formats
All OPCODEs are the same – select R-type
FN3 defines the basic ALU operation
FN7 defines additional instructions

## Slide 17: RISC-V I-type instructions
Immediate arithmetic and load instructions
  rs1: source or base address register number
  immediate: constant operand, or offset added to base address
    2s-complement, sign extended
immediate
rs1
rd
funct3
opcode
12 bits
7 bits
5 bits
5 bits
3 bits

## Slide 18: RISC-V I-type instruction example
addi x5, x0, 1024
  <rd> = <rs1> + 1024
  opcode + funct3 define the instruction as addi
rd rs1 constant
immediate
rs1
rd
funct3
opcode
12 bits
7 bits
5 bits
5 bits
3 bits
1024
0
5
funct3
opcode
12 bits
7 bits
5 bits
5 bits
3 bits

## Slide 19: RISC-V I-type instruction example
lw x5, 32(x18)
  <rd> = memory(<rs1> + 32)
  opcode + funct3 define the instruction as lw
rd constant rs1
immediate
rs1
rd
funct3
opcode
12 bits
7 bits
5 bits
5 bits
3 bits
32
18
5
funct3
opcode
12 bits
7 bits
5 bits
5 bits
3 bits

## Slide 20: RISC-V I-type instruction example
jalr x5, 32(x18)
  <rd> = PC + 4
  PC = <rs1> + constant
rd constant rs1
immediate
rs1
rd
funct3
opcode
12 bits
7 bits
5 bits
5 bits
3 bits

## Slide 21: RISC-V I-type Immediate Instruction Formats
All OPCODEs are the same – select I-type immediate
FN3 defines the basic ALU operation
  Same as equivalent R-type operation
Shift immediates only 5/6-bits
FN7 defines additional shift instructions

## Slide 22: RISC-V I-type Load Instruction Formats
All OPCODEs are the same – select I-type load
  NOTE: Adjacent to 0010011 of I-type immediate format (1 bit difference)
FN3 defines the type of load

## Slide 23: RISC-V I-type JALR Instruction Formats
OPCODE – selects I-type jalr
  NOTE: Not adjacent to others
FN3 must be 000 – allows for future instructions

## Slide 24: RISC-V S-type instructions
Different immediate format for store instructions
  rs1: base address register number
  rs2: source operand register number
  imm(ediate): offset added to base address – split for alignment with other instructions
  Need rs2 but not rd
  Keep rs2 in the same place in all instructions
rs2
rs1
funct3
opcode
7 bits
7 bits
5 bits
5 bits
5 bits
3 bits
imm[11:5]
imm[4:0]

## Slide 25: RISC-V S-type Store Instruction Formats
All OPCODEs are the same – select S-type store
FN3 defines the type of store (same as for load)
rs2 is in the standard location
Immediate field is split to allow rs2

## Slide 26: RISC-V Memory Store Operation Details
Assume x7 contains 0x12345678
Assume x6 contains 0x500
sw x7, 0x20(x6) - what address?
What changes in memory?
a
b
c
d
e
f
g
h
i
j
k
l
m
n
o
p
0
1
2
3
0x520
0x524
0x528
0x52C
Data in Memory

## Slide 27: RISC-V Memory Store Operation Details
Assume x7 contains 0x12345678
Assume x6 contains 0x500
sw x7, 0x20(x6) - what address?
What changes in memory?
sh x7, 0x26(x6) – what address?
What changes in memory?
78
56
34
12
e
f
g
h
i
j
k
l
m
n
o
p
0
1
2
3
0x520
0x524
0x528
0x52C
Data in Memory

## Slide 28: RISC-V Memory Store Operation Details
Assume x7 contains 0x12345678
Assume x6 contains 0x500
sw x7, 0x20(x6) - what address?
What changes in memory?
sh x7, 0x26(x6) – what address?
What changes in memory?
sb x7, 0x2d(x6) – what address?
What changes in memory?
78
56
34
12
e
f
78
56
i
j
k
l
m
n
o
p
0
1
2
3
0x520
0x524
0x528
0x52C
Data in Memory

## Slide 29: RISC-V Memory Store Operation Details
Assume x7 contains 0x12345678
Assume x6 contains 0x500
sw x7, 0x20(x6) - what address?
What changes in memory?
sh x7, 0x26(x6) – what address?
What changes in memory?
sb x7, 0x2d(x6) – what address?
What changes in memory?
78
56
34
12
e
f
78
56
i
j
k
l
m
78
o
p
0
1
2
3
0x520
0x524
0x528
0x52C
Data in Memory

## Slide 30: RISC-V Memory Load Operation Details
Assume x6 contains 0x500
  lw x7, 0x2C(x6) - what goes to x7?
  0x87547827
  lhu x7, 0x24(x6) – what goes to x7?
  0x0000BC9A
  lh x7, 0x24(x6) – what goes to x7?
  0xFFFFBC9A
  lbu x7, 0x2F(x6) – what goes to x7?
  0x00000087
  lb x7, 0x21(x6) – what goes to x7?
  0x00000056
78
56
34
12
9A
BC
78
56
i
j
k
l
27
78
54
87
0
1
2
3
0x520
0x524
0x528
0x52C
Data in Memory

## Slide 31: RISC-V: B-type Instructions
B-type (SB-type in the textbook)
Branch instructions specify
  Opcode, two registers, target address
Most branch targets are near branch
  Forward or backward
PC-relative addressing
  Target address = PC + immediate × 2
Example of Making the Common Case Fast
rs2
rs1
funct3
opcode
imm [10:5]
imm [4:1]
imm[12]
imm[11]

## Slide 32: RISC-V: B-type Instructions
Why times 2??
  A branch addresses an instruction
  Instructions are at least 16 bits (32 in our design)
  So on a 16-bit boundary
  Addresses are therefore even, i.e. bit 0 is always 0
  So don’t need bit 0, and can extend the branch distance with bit 12
  Move bit 11 for alignment with other instructions
rs2
rs1
funct3
opcode
imm [10:5]
imm [4:1]
imm[12]
imm[11]

## Slide 33: RISC-V B-type Branch Instruction Formats
All OPCODEs are the same – select B-type branch
FN3 defines the type of branch
Offset (immediate) is arranged to maximize alignment with other formats
Offset has no bit 0 – times 2 addressing

## Slide 34: RISC-V: J-type Instruction (JAL)
Jump and link (JAL) instruction uses 20-bit immediate
J-type (UJ type in textbook)
Offset is times 2 just as for branches
For long jumps, e.g., to 32-bit absolute address 0x12345678
  lui x8, 0x12345: load address[31:12] to temp register x8
  jalr x0, 0x678(x8): add address[11:0] and jump to target
rd
opcode
7 bits
5 bits
imm[11]
imm[20]
imm[10:1]
imm[19:12]

## Slide 35: RISC-V J-type Instruction Formats
OPCODE – selects J-type jal (no FN3)
  NOTE: Adjacent to jalr
Branch offset scrambled to optimize alignment with other formats