## Slide 1: ECEN 4593-001 Computer Organization
Lecture #8
3 February 2021

## Slide 2: Agenda
Class Announcements
Class Project Phase 2
RISC-V instruction Formats

## Slide 3: Class Announcements
Reading for the week
  “Computer Organization and Design, The Hardware / Software Interface, RISC-V edition,” by David Patterson and John Hennessy
    ISBN 978-0-12-812275-4
    Chapter 2, “Language of the Computer”
      sections 2.1 thru 2.8
      pages 60-108 (sections 2.1 thru 2.8)
My OH will be on Zoom from 2:00 to 3:00 today
https://cuboulder.zoom.us/j/4317981384
Request – enable your cameras

## Slide 4: Class Announcements
Phase 2 is posted
The Target Date is Sunday, February 7 at 10:00 PM
Bonus 1%/day before that. Deduction 10%/day after that. (POLL)
Phase 3 is posted
The Target Date is Sunday, February 14 at 10:00 PM
Bonus 1%/day before that. Deduction 5%/day after that.
Also other completion metrics which affect the score
Homework #1 is due tomorrow, February 4 at 10:00 PM

## Slide 5: Homework #1 - Endianness
Alignment in the processor is always the same – it’s only different in memory
No byte is ever changed – every byte read must have been written (except for 00 and ff).

## Slide 6: Phase 2 Notes
Class Project section “Debug” in Canvas
Document there – “Basic Software Debug”
A value in memory must be correct for a successful submission
Document there – “Memory Debug”
Everything you need is in each section of ia_utils.codal.

## Slide 7: Debugging
Debug Process
  Determine where the error is (x10 in Phase 2 tells you the case)
  Determine what the expected result is
  Identify what the actual result is
THEN examine the code related to the failing function

## Slide 8: Class Project – isa.codal
The decoder is riscv_isa in isa.codal
Compares the input (the instruction) to all elements in riscv_isa
Calls the matching element
Uncomment the remaining elements, except for CSRs

## Slide 9: Class Project – isa.codal
isa.codal instruction element (group)
Which instructions are in it
Assembly definition
Machine code definition
Instruction execution

## Slide 10: Class Project – opcodes.hcodal
opcodes.hcodal
  Defines the opcode (17 bits)
Uncomment
Complete each instruction
  Define internal constants
  Assemble into instruciton

## Slide 11: Class Project – ia_utils.codal
ia_utils.codal
Add function for each instruction
Functions from the comments below
Do not add or modify functions

## Slide 12: Class Project
ia_main_reset
  Fetch an instruction
  Increment the PC
  Execute the decode (riscv_isa function in isa.codal)
  Jump back
Repeat until stop

## Slide 13: Class Project
If the simulation stops here (in ia_main_reset.codal):
You have fetched an illegal instruction
You have a bad instruction definition in opcodes.hcodal
You have an incorrect operation in isa.codal
Step to see which instruction causes this, and check that instruction carefully

## Slide 14: Codasip Search Function
Select Search function
Select “File”
Enter string to search
Shows all instances in Console

## Slide 15: RISC-V: U-type Instructions
LUI – (IMM[31:12] :: 000000000000)  rd
AUIPC – (IMM[31:12] :: 000000000000) + PC  rd
Why add a constant to the PC in AUIPC?
Regularity!
opcode
rd
immediate[31:12]

## Slide 16: RISC-V U-type Instruction Formats
OPCODE – selects individual instructions (no FN3)
  NOTE: LUI/AUIPC adjacent
Upper immediate aligned with data path

## Slide 17: RISC-V: Addressing Summary

## Slide 18: Definitions
Immediate addressing: where an operand is a constant within the instruction
Register addressing: where the operand(s) is a register
Base or displacement addressing: where the operand is at the memory location whose address is the sum of a register and a constant in the instruction
PC-relative addressing: where the branch address is the sum of the PC, Program Counter, and a constant in the instruction

## Slide 19: RISC-V Instruction Formats
OPCODE – selects format type in all cases
All fields are always aligned if they exist
Design Principle 1: Simplicity favors regularity
  Regularity makes implementation simpler
  Regularity makes pipelining possible
  Simplicity enables higher performance at lower cost

## Slide 20: RISC-V Small Immediates
Standard immediate is small (12 bits)
Why not larger (NIOS is 16 bits)?
Design Principle 2: Smaller is Faster
  Small constants are common
Reduces available bits for other funcitons
Another good reason for only 32 registers (64 wouldn’t fit)

## Slide 21: RISC-V Instruction Formats
Why not one consistent format?
Design Principle 3: Good design demands good compromises
  Different formats complicate decoding, but allow 32-bit instructions uniformly
  Keep formats as similar as possible

## Slide 22: RISC-V Complex Immediates
Immediates are complex and seem difficult to handle
Simplifies the hardware by making instruction fields align
The sign is always the upper bit
Different immediates require only multiplexors which are fast
Only the Assembler author and the hardware designer care
Programmers see the Abstraction of Assembly Language